# Two-Day Seminar on

# Testing Analog and Digital Products

# By Professor Vishwani D. Agrawal

Penang, July 12-13, 2005

Test 2				Student’s name __________________________________

# Note: Please attempt all questions.

Question 1: Specify a simple method that will make a sequential circuit initializable by just a single input vector, irrespective of its cyclic structure?

Answer: Use all flip-flops with either a reset or clear input and connect all those inputs to a primary input pin.

# Question 2: Without using time-frame expansion, find a test for the fault a stuck-at-1?

Answer: A two-vector test, {a,b} = {X,0}, {0,0} will detect the fault a stuck-at-1. The first vector will initialize the flip-flop output to 0, and the second vector will activate the fault whose effect will be propagated to the primary output f.

Question 3: A circuit contains n+k flip-flops of which n form a shift register. What is the minimum number of scan flip-flops needed for scan design?

Answer: k+1. The first flip-flop of the shift register and all other isolated flip-flops should be replaced by scan flip-flops.

# Text boxes

a

b

c

d

e

f

Flip-flop

clock