## Slide 1: Reduced Voltage Test Can be Faster!
Vishwani D. Agrawal
vagrawal@eng.auburn.edu
Support from NSF Grant 1116213

## Slide 2: Effects of Reducing Supply Voltage
Critical path slows down.
Power reduces as V2.
Test produces more than functional activity; consumes more power that the circuit is designed for.
Test clock is slower due to power constrain.

## Slide 3: Power and Frequency vs. Voltage
Voltage VDD
Max. clock frequency
(structure constrained)
Peak power/cycle during test
PMAXfunc
Nominal
voltage
Vtest
Power constrained
test
Structure
constrained
test

## Slide 4: Reduced Voltage Test Results
Circuit (180nm CMOS) | PMAX per cycle (mW) | 1.8V test freq. (MHz) | Test voltage (volts) | Test clock freq. (MHz) | Test time reduction (%)
s298 | 1.2 | 187 | 1.08 | 500 | 62.5
s13207 | 21.3 | 110 | 1.45 | 165 | 40.3
s38584 | 110.6 | 129 | 1.50 | 187 | 31.0
P. Venkataramani and V. D. Agrawal, “Reducing Test Time of Power Constrained
Test by Optimal Selection of Supply Voltage,” Proc. 26th International Conf.
VLSI Design, January 2013.