## Slide 1
Polynomial-Time Algorithms for Designing Dual-Voltage Energy Efficient Circuits
Master’s Thesis Defense
Mridula Allani
Advisor : Dr. Vishwani D. Agrawal
Committee Members: Dr. Victor P. Nelson, Dr. Adit D. Singh
Department of Electrical and Computer Engineering
Auburn University
October 19, 2011

## Slide 2: Outline
Motivation
Problem statement
Background
Contributions
  Algorithm to find VDDL
  Algorithm to assign VDDL
Results
Future work
References

## Slide 3: Motivation
Ref. http://www.anandtech.com/show/3794/the-iphone-4-review/13

## Slide 4: Motivation
Current dual voltage designs use 0.7VDD as the lower supply voltage.
Algorithms to assign low voltage have exponential or polynomial complexity.
Require faster algorithms that increase energy savings.

## Slide 5: Problem Statement
Develop a linear time algorithm to find the optimal lower voltage.
Develop new algorithms for voltage assignment in dual-VDD design.

## Slide 6: Background
Gate slack:
  The amount of time by which a signal is early or late.
Critical path:
  The longest path in the circuit.
  All gates on this path have ‘zero’ slack.
Timing constraints:
  No other path can be longer than the critical path.
  No gate should have a negative slack.

## Slide 7: Background
Timing violations:
  A path is longer than the critical path.
  The gates on this path have negative slack.
Topological constraints:
  NoVDDL gate is at the input of any VDD gate.
Estimate of energy savings (neglecting leakage):
where N is the number of gates in low voltage and n is
the total number of gates.

## Slide 8: Background
Basic idea: decrease energy consumption without any delay penalty.
Done by assigning lower supply voltage to gates on non-critical paths.
Different algorithms propose different ways of finding these non-critical gates.

## Slide 9: Background
Authors Kuroda and Hamada say that power reduction ratio
is minimum when 0.6VDD ≤ VDDL ≤ 0.7VDD .
The works described by Chen, et. al., Kulkarni, et. al., Srivatsava, et. al., claims that the optimal value of VDDL for minimizing total power is 50% of VDD.
Rule of thumb proposed by Hamada, et. al. says

## Slide 10: Background
CVS Structure
[Usami and Horowitz]
ECVS Structure [Usami, et. al.]
VDDL
VDD
Level Converter
Ref. K. Usami and M. Horowitz, “Clustered Voltage Scaling Technique for Low-Power Design," in Proceedings of the International Symposium on Low Power Design, pp. 23-26, 1995.
Ref. K. Usami, et. al.,“Automated Low-Power Technique Exploiting Multiple Supply Voltages Applied to a Media Processor," IEEE Journal of Solid-State Circuits, vol. 33, no. 3, pp. 463-472, Mar. 1998.

## Slide 11: Background
Kulkarni, et al.
  Greedy heuristic based on gate slacks.
  Uses 0.7VDD and 0.5VDD as VDDL.
  Includes power and delay overhead of level converters.
Sundararajan and Parhi
  Linear programming based model.
  Minimizes the power consumption.
  Includes level converter delay overheads.

## Slide 12: Background
TPI (i): longest time for an event to arrive at gate i from PI.
TPO (i): longest time for an event from gate i to reach PO.
Slack time for gate i: Si = Tc – Dp,i , where Tc = Max { Dp,i } for all i
[Kim and Agrawal]
Delay of the longest path through gate i : Dp,i = TPI(i) + TPO(i)
TPI (i)
TPO (i)
Tc
PI
PO

## Slide 13: Background
Su, the upper slack time is the lower bound of slacks of the gates which can be unconditionally assigned low voltage without affecting the critical timing of the circuit.
where β = D’p,I / Dp,i and D’p,i, Dp,i is the longest path delay through the gate i when it is supplied with VDDL and VDD, respectively.
[Kim and Agrawal]
Chart: Su Vs. VDDL
Su = Tc
Notes: Maximum over all gates

## Slide 14: Background
Recent work [Kim and Agrawal]:
  Assign VDDL to gates with Si ≥Su.
  Assign VDDL to gates with Sl ≤ Si ≤ Su one by one without violating timing or topological constraints.
  Repeat last two steps across all voltages to find the best VDDL and the corresponding dual-voltage design with the least energy.
Ref. K. Kim and V. D. Agrawal, “Dual Voltage Design for Minimum Energy Using Gate Slack,” in Proceedings of the IEEE International Conference on Industrial Technology, pp. 419-424 , March, 2011.

## Slide 15: Example
Without level converter
V1
V1
V1
V1
V1
V2
V2
V2
V2
V2
IN
OUT

## Slide 16: Example: Energy per cycle and delay
Without level converter
9.69fJ ∞ | 44.84fJ 280.6ps | 15.75fJ 123.7ps | 7.315fJ 95.61ps | 7.863fJ 84.15ps
6.465fJ ∞ | 10.13fJ 204.5ps | 4.573fJ 123.2ps | 5.203fJ 99.28ps | 6.65fJ 91.19ps
6.6fJ 1183ps | 2.651fJ 203.3ps | 3.233fJ 132.3ps | 4.289fJ 115ps | 5.678fJ 107.7ps
1.291fJ 801.5ps | 1.761fJ 235.4ps | 2.543fJ 179.4ps | 3.567fJ 164.3ps | 4.977fJ 156.1ps
0.755fJ 1062ps | 1.285fJ 614 ps | 2.052fJ 565.3ps | 3.082fJ 560.5ps | 4.423fJ 557.7ps
V2(V)
V1(V)
0.4
0.6
0.8
1.0
1.2
0.4
0.6
0.8
1.0
1.2
90 nm PTM model
Clock period: 1500 ps

## Slide 17: Example
With level converter
V1
V1
V1
V1
V1
V2
V2
V2
V2
V2
IN
OUT
LC(V1,V2)

## Slide 18: Example
10.44fJ ∞ | 7.18fJ 249.1ps | 7.18fJ 184.0ps | 7.98fJ 161.7ps | 9.316fJ 153.4ps
7.13fJ 1198ps | 4.39fJ 268.5ps | 4.96fJ 203.3ps | 5.94fJ 182.8ps | 8.05fJ 174.8ps
2.74fJ 952.5ps | 2.83fJ 309.4ps | 3.56fJ 251.4ps | 4.93fJ 231.8ps | 16.14fJ 225.8ps
1.408fJ 948.8ps | 1.91fJ 470.7ps | 2.82fJ 418.9ps | 10.34fJ 405.7ps | 45.31fJ 387.8ps
0.81fJ 2188ps | 1.4fJ 1757ps | 7.08fJ 1733ps | 6.46fJ ∞ | 9.75fJ ∞
9.69fJ ∞ | 44.84fJ 280.6ps | 15.75fJ 123.7ps | 7.315fJ 95.61ps | 7.863fJ 84.15ps
6.465fJ ∞ | 10.13fJ 204.5ps | 4.573fJ 123.2ps | 5.203fJ 99.28ps | 6.65fJ 91.19ps
6.6fJ 1183ps | 2.651fJ 203.3ps | 3.233fJ 132.3ps | 4.289fJ 115ps | 5.678fJ 107.7ps
1.291fJ 801.5ps | 1.761fJ 235.4ps | 2.543fJ 179.4ps | 3.567fJ 164.3ps | 4.977fJ 156.1ps
0.755fJ 1062ps | 1.285fJ 614 ps | 2.052fJ 565.3ps | 3.082fJ 560.5ps | 4.423fJ 557.7ps
0.4
0.6
0.8
1.0
1.2
0.4
0.6
0.8
1.0
1.2
With level converter
Without level converter
0.4
0.6
0.8
1.0
1.2
V2(V)
V1(V)

## Slide 19: Outline
Motivation
Problem statement
Background
Contributions
  Algorithm to find VDDL
  Algorithm to assign VDDL
Results
Future work
References

## Slide 20: Grouping of gates
Chart: c880
 | 0 | 100 | 300 | 500
 | 0 | 100 | 300 | 500
45o line
Su = 336.9 ps
P
G
≥0
∑(dli–dhi)≤min{Si}
Notes: Full paths
CVS gates begin from PI

## Slide 21: Groups when VDDL = 1.2V
Chart: c880
 | 0 | 100 | 300 | 500
 | 0 | 100 | 300 | 500
45o line
P
G
VDD = 1.2V
VDDL = 1.2V
Tc = 510 ps
Su = 0 ps
Notes: Full paths
CVS gates begin from PI

## Slide 22: Groups when VDDL = 1.19V
Chart: c880
 | 0 | 100 | 300 | 500
 | 0 | 100 | 300 | 500
45o line
P
G
VDD = 1.2V
VDDL = 1.19V
Tc = 510 ps
Su = 14.6 ps
Notes: Full paths
CVS gates begin from PI

## Slide 23: Groups when VDDL = 0.49V
Chart: c880
 | 0 | 100 | 300 | 500
 | 0 | 100 | 300 | 500
45o line
Su = 336.9 ps
P
G
Tc = 510 ps
Notes: Full paths
CVS gates begin from PI

## Slide 24: Groups when VDDL = 0.39V
Chart: c880
 | 0 | 100 | 300 | 500
 | 0 | 100 | 300 | 500
45o line
P
G
VDD = 1.2V
VDDL = 0.39V
Su = 469ps
Tc = 510 ps
Notes: Full paths
CVS gates begin from PI

## Slide 25: Groups when VDDL = 0.1V
Chart: c880
 | 0 | 1000 | 5000 | 140000
 | 0 | 1000 | 5000 | 140000
G
VDD = 1.2V
VDDL = 0.1V
Su = 510 ps = Tc
Tc = 510 ps
P
45o line
Notes: Full paths
CVS gates begin from PI

## Slide 26: Theorems
1. Gates above the 45o line in the ‘Delay increment versus
slack’ plot cannot be assigned lower supply voltage without violating the timing constraint.
2.
where βi = dli/dhi and dli is the low voltage delay and dhi is the high voltage delay of gate i. The maximum value of βi; βmax, will give us the lower bound on the gate slacks.

## Slide 27: Theorems
3. Groups within P which satisfy
can be assigned lower supply voltage without violating
the timing constraint. (where, yi = dli – dhi , dli = low
voltage delay of gate i, dhi = high voltage delay of
gate i and Si = slack of the gate i at VDD.)
4. Group with slacks greater than Su, G, can always be
assigned the lower supply voltage without causing any
topological violations.
Notes: Theorem 4

## Slide 28: Algorithm to find VDDL
Assume all gates are assigned VDD initially.
Calculate the gate slacks.
Group the gates according to their slacks and delays.

## Slide 29: Algorithm to find VDDL
VDDL = VDDL1, when using no level converter.
VDDL = (VDDL1VDDL2)1/2, when using level converter.

## Slide 30: Algorithm to find VDDL
=VDD
C880
Total 360 gates
Notes: Energy saving ratio per gate

## Slide 31: Algorithm to find VDDL
=VDD
C880
Total 360 gates
VDDL1= 0.49V
VDDL2= 0.71V
Notes: Vl1 and vl2 in graph.

## Slide 32: Results: VDDL selection algorithm
ISCAS’85 | Total gates | Without level converters |  |  |  |  |  |  |  |  |  |  | 
 |  | VDDL = VDDL1 |  |  | VDDL = VDDL2 |  |  | VDDL= (VDDL1+VDDL2 )/2 |  |  | VDDL = (VDDL1VLDD2)1/2 |  | 
 |  | VDDL (V) | Gates in VDDL | Esav(%) | VDDL (V) | Gates in VDDL | Esav(%) | VDDL (V) | Gates in VDDL | Esav (%) | VDDL (V) | Gates in VDDL | Esav (%)
C432 | 154 | 0.80 | 8 | 2.9 | 0.89 | 8 | 2.3 | 0.84 | 8 | 2.7 | 0.84 | 8 | 2.7
C499 | 493 | 0.76 | 113 | 13.7 | 1.11 | 141 | 4.1 | 0.93 | 123 | 10.0 | 0.91 | 129 | 11.1
C880 | 360 | 0.49 | 213 | 49.3 | 0.71 | 229 | 41.3 | 0.6 | 229 | 47.7 | 0.58 | 229 | 48.8
C1355 | 469 | 0.77 | 76 | 9.5 | 1.11 | 108 | 3.4 | 0.94 | 76 | 6.3 | 0.92 | 76 | 6.7
C1908 | 584 | 0.60 | 221 | 28.4 | 1.00 | 221 | 11.6 | 0.80 | 221 | 21.9 | 0.77 | 221 | 22.3
C2670 | 901 | 0.48 | 570 | 53.1 | 0.82 | 570 | 33.7 | 0.65 | 570 | 44.7 | 0.62 | 570 | 46.4
C3540 | 1270 | 0.52 | 149 | 9.5 | 0.73 | 149 | 7.4 | 0.62 | 149 | 8.6 | 0.61 | 149 | 8.7
C5315 | 2077 | 0.49 | 1220 | 49.0 | 0.75 | 1226 | 36.0 | 0.62 | 1220 | 43.1 | 0.60 | 1220 | 44.1
C6288 | 2407 | 0.55 | 75 | 2.5 | 1.00 | 77 | 0.98 | 0.77 | 77 | 1.9 | 0.73 | 77 | 2.0
C7288 | 2823 | 0.54 | 1582 | 44.7 | 0.71 | 2123 | 8.9 | 0.62 | 1672 | 43.4 | 0.61 | 1672 | 43.4

## Slide 33: Results: VDDL selection algorithm
ISCAS’85 | Total gates | With level converters |  |  |  |  |  |  |  |  |  |  | 
 |  | VDDL = VDDL1 |  |  | VDDL = VDDL2 |  |  | VDDL= (VDDL1+VDDL2 )/2 |  |  | VDDL = (VDDL1VLDD2)1/2 |  | 
 |  | VDDL (V) | Gates in VDDL | Esav(%) | VDDL (V) | Gates in VDDL | Esav(%) | VDDL (V) | Gates in VDDL | Esav (%) | VDDL (V) | Gates in VDDL | Esav (%)
C432 | 154 | 0.80 | 73 | 17.1 | 0.89 | 85 | 24.8 | 0.84 | 81 | 26.8 | 0.84 | 81 | 26.8
C499 | 493 | 0.76 | 173 | 21.1 | 1.11 | 359 | 10.5 | 0.93 | 249 | 20.2 | 0.91 | 247 | 21.3
C880 | 360 | 0.49 | 223 | 51.6 | 0.71 | 309 | 55.8 | 0.6 | 290 | 60.4 | 0.58 | 286 | 60.9
C1355 | 469 | 0.77 | 122 | 15.3 | 1.11 | 260 | 8.0 | 0.94 | 197 | 16.3 | 0.92 | 193 | 17.0
C1908 | 584 | 0.60 | 263 | 33.8 | 1.00 | 267 | 24.4 | 0.80 | 395 | 37.6 | 0.77 | 385 | 38.8
C2670 | 901 | 0.48 | 376 | 35.1 | 0.82 | 784 | 46.4 | 0.65 | 677 | 53.1 | 0.62 | 633 | 51.5
C3540 | 1270 | 0.52 | 647 | 41.4 | 0.73 | 1073 | 53.2 | 0.62 | 906 | 52.3 | 0.61 | 881 | 51.5
C5315 | 2077 | 0.49 | 1140 | 45.0 | 0.75 | 1777 | 52.1 | 0.62 | 1633 | 57.6 | 0.60 | 1602 | 57.8
C6288 | 2407 | 0.55 | 659 | 21.6 | 1.00 | 1877 | 23.8 | 0.77 | 1302 | 31.8 | 0.73 | 1189 | 47.3
C7288 | 2823 | 0.54 | 1560 | 44.1 | 0.71 | 2235 | 51.5 | 0.62 | 1998 | 51.9 | 0.61 | 1197 | 51.8

## Slide 34: Results: Comparison with reported data
ISCAS’85 | Total gates | Without level converters |  |  |  |  |  | 
 |  | VDDL=VDDL1 |  |  | VDDL= VDDL = 0.7VDD = 0.84V |  | VDDL= VDDL = 0.5VDD = 0.6V | 
 |  | VDDL (V) | Gates in VDDL | Esav (%) | Gates in VDDL | Esav ( %) | Gates in VDDL | Esav (%)
C432 | 154 | 0.80 | 8 | 2.9 | 8 | 2.7 | 8 | 3.9
C499 | 493 | 0.76 | 113 | 13.7 | 121 | 12.5 | 56 | 8.5
C880 | 360 | 0.49 | 213 | 49.3 | 229 | 32.4 | 229 | 47.7
C1355 | 469 | 0.77 | 76 | 9.5 | 76 | 8.3 | 64 | 10.2
C1908 | 584 | 0.60 | 221 | 28.4 | 221 | 19.3 | 221 | 28.4
C2670 | 901 | 0.48 | 570 | 53.1 | 570 | 32.3 | 570 | 47.5
C3540 | 1270 | 0.52 | 149 | 9.5 | 149 | 6.0 | 149 | 8.8
C5315 | 2077 | 0.49 | 1220 | 49.0 | 1240 | 30.5 | 1220 | 44.1
C6288 | 2407 | 0.55 | 75 | 2.5 | 77 | 1.6 | 75 | 2.3
C7288 | 2823 | 0.54 | 1582 | 44.7 | 2359 | 42.6 | 1672 | 43.9

## Slide 35: Results: Comparison with reported data
ISCAS’85 | Total gates | With level converters |  |  |  |  |  | 
 |  | VDDL=VDDL1 |  |  | VDDL=VDDL = 0.7VDD = 0.84V |  | VDDL=VDDL = 0.5VDD = 0.6V | 
 |  | VDDL (V) | Gates in VDDL | Esav (%) | Gates in VDDL | Esav ( %) | Gates in VDDL | Esav (%)
C432 | 154 | 0.84 | 81 | 26.8 | 81 | 26.8 | 43 | 20.9
C499 | 493 | 0.91 | 247 | 21.3 | 211 | 21.2 | 99 | 15.1
C880 | 360 | 0.58 | 286 | 60.9 | 323 | 45.8 | 290 | 60.4
C1355 | 469 | 0.92 | 193 | 17.0 | 154 | 16.8 | 44 | 7.0
C1908 | 584 | 0.77 | 385 | 38.8 | 415 | 36.2 | 263 | 33.8
C2670 | 901 | 0.62 | 633 | 51.5 | 813 | 46.0 | 606 | 50.5
C3540 | 1270 | 0.61 | 881 | 51.5 | 1093 | 43.9 | 864 | 51.0
C5315 | 2077 | 0.60 | 1602 | 57.8 | 1812 | 44.5 | 1602 | 56.9
C6288 | 2407 | 0.73 | 1189 | 47.3 | 1470 | 31.2 | 780 | 24.3
C7288 | 2823 | 0.61 | 1197 | 51.8 | 2347 | 42.4 | 1943 | 51.6

## Slide 36: Outline
Motivation
Problem statement
Background
Contributions
  Algorithm to find VDDL
  Algorithm to assign VDDL
Results
Future work
References

## Slide 37: Algorithm to assign VDDL
Assume all gates are at VDD initially.
Calculate slacks of all gates.
Assign VDDL to gates whose slacks,
Si ≥Su
Recalculate slacks.

## Slide 38: Algorithm to assign VDDL
Assign VDDL to a group of gates in P satisfying the condition
Recalculate slacks.
Check whether there are any VDDL gates at the inputs of any VDD gates and if there are any negative slacks.

## Slide 39: Algorithm to assign VDDL
If there any violations occur, put the corresponding gate back to VDD .
Recalculate slacks.
Repeat previous five steps until we do not have any VDD gates in groups P and G.

## Slide 40: c880 slack distribution
Chart: Initial Slack of c880
 | 0 | 100 | 300 | 500
 | 0 | 100 | 300 | 500
45o line
Su =336.9 ps
P
G
VDD = 1.2V
VDDL = 0.49V

## Slide 41: Slack data after VDDL assignment
Chart: Final Slack of c880
 | 0 | 100 | 300 | 500
 | 0 | 100 | 300 | 500
45o line
Su = 336.9ps
P
G
VDD = 1.2V
VDDL = 0.49V

## Slide 42: Dual voltage design without level converter
ISCAS’85 | Total gates | VDDL=VDDL1 Determination and assignment |  |  |  | SPICE Results ** |  |  | [Kim and Agrawal] | 
 |  | VDDL (V) | Gates in VDDL | Esav (%) | CPU* (s) | Esingle VDD (fJ) | Edual VDD( fJ) | Esav (%) | Esav (%) | CPU (s)
C432 | 154 | 0.80 | 8 | 2.9 | 1.78 | 161.3 | 155.4 | 3.7 | 3.9 | 15.8
C499 | 493 | 0.76 | 113 | 13.7 | 9.41 | 463 | 427 | 7.8 | 5.9 | 194.4
C880 | 360 | 0.49 | 213 | 49.3 | 5.39 | 277.6 | 115.8 | 58.3 | 50.8 | 62.1
C1355 | 469 | 0.77 | 76 | 9.5 | 8.75 | 455.2 | 433.1 | 4.9 | 4.3 | 132
C1908 | 584 | 0.60 | 221 | 28.4 | 11.43 | 496.5 | 378.3 | 23.8 | 19.0 | 247.8
C2670 | 901 | 0.48 | 570 | 53.1 | 23.49 | 660.3 | 251.5 | 61.9 | 47.8 | 480.7
C3540 | 1270 | 0.52 | 149 | 9.5 | 45.44 | 1843 | 1620 | 12.2 | 9.6 | 1244
C5315 | 2077 | 0.49 | 1220 | 49.0 | 109.47 | 2320 | 1272 | 45.2 | N/R | N/R
C6288 | 2407 | 0.55 | 75 | 2.5 | 154.94 | 1932 | 1869 | 3.3 | 2.6 | 6128
C7288 | 2823 | 0.54 | 1582 | 44.7 | 191.04 | 2465 | 1562 | 36.6 | N/R | N/R
Intel Core i5 2.30GHz, 4GB RAM
**90nm PTM model

## Slide 43: CPU Time Vs. Number of Gates
Chart: Number of gates
| 160 | 202 | 383 | 546 | 880 | 1211 | 1705 | 2341 | 2416 | 3624
Sundararajan and Parhi | 7.83 | 10.1 | 54.4 | 47.2 | 739 | 1229 | 1743 | 4243 | 7736 | 9475
Our algorithm | 1.78 | 9.41 | 5.39 | 8.75 | 11.43 | 23.49 | 45.44 | 109.47 | 154.94 | 191.04
Kim and Agrawal | 15.8 | 194.4 | 62.1 | 132 | 247.8 | 480.7 | 1244 | 6128

## Slide 44: c880 slacks with 5% increase in Tc
Chart: Slack (ps)
 | 0 | 100 | 300 | 500
 | 0 | 100 | 300 | 500
45o line
Su = 293ps
P
G
VDD = 1.2V
VDDL = 0.67V

## Slide 45: c880 final slacks with 5% increase in Tc
Chart: Slack (ps)
High voltage gates | 51.54 | 30.07 | 10.298 | 19.19 | 19.19 | 14.64 | 19.19 | 30.07 | 33.65 | 19.19 | 30.07 | 10.298 | 29.64 | 14.64 | 19.01 | 35.01
 | 0 | 100 | 300 | 500
 | 0 | 100 | 300 | 500
45o line
Su = 293ps
P
G
VDD = 1.2V
VDDL = 0.67V

## Slide 46: Dual voltage design without level converter with 5% increase in Tc
ISCAS’85 | Total gates | VDDL=VDDL1 Determination and assignment |  |  |  | SPICE Results ** |  | 
 |  | VDDL (V) | Gates in VDDL | Esav (%) | CPU* (s) | Esingle VDD (fJ) | Edual VDD (fJ) | Esav (%)
C432 | 154 | 1.08 | 154 | 19.0 | 1.70 | 161.3 | 123.9 | 23.2
C499 | 493 | 1.03 | 493 | 26.3 | 9.18 | 463 | 321.9 | 30.5
C880 | 360 | 0.67 | 334 | 65.8 | 4.32 | 277.6 | 83.86 | 69.8
C1355 | 469 | 1.06 | 469 | 22.0 | 8.52 | 455.2 | 339.9 | 12.2
C1908 | 584 | 1.00 | 584 | 30.6 | 8.56 | 496.5 | 445 | 10.4
C2670 | 901 | 0.81 | 899 | 54.3 | 15.81 | 660.3 | 257.3 | 61.0
C3540 | 1270 | 0.90 | 1270 | 43.8 | 28.22 | 1843 | 949.5 | 48.5
C5315 | 2077 | 0.72 | 2077 | 64.0 | 61.77 | 2320 | 716.8 | 69.1
C6288 | 2407 | 1.07 | 2407 | 20.5 | 108.39 | 1932 | 1464 | 24.2
C7288 | 2823 | 0.68 | 2816 | 67.7 | 175.07 | 2465 | 677.2 | 72.3
Intel Core i5 2.30GHz, 4GB RAM
**90nm PTM model

## Slide 47: Future work
Accommodate level converter energy overheads.
Consider leakage energy reduction.
Dual threshold designs.
Simultaneous dual supply voltage and dual threshold voltage designs.
Include the effects of process variations.

## Slide 48: References
T. Kuroda and M. Hamada, “Low-Power CMOS Digital Design with Dual Embedded Adaptive Power Supplies," IEEE Journal of Solid-State Circuits, vol. 35, no. 4, pp. 652-655, Apr. 2000.
M. Hamada, Y. Ootaguro, and T. Kuroda, “Utilizing Surplus Timing for Power Reduction,” in Proceedings of the IEEE Custom Integrated Circuits Conference, pp. 89-92, 2001.
C. Chen, A. Srivastava, and M. Sarrafzadeh, “On Gate Level Power Optimization Using Dual-Supply Voltages," IEEE Transactions on Very Large Scale Integration (VLSI) Systems, vol. 9, no. 5, pp. 616-629, Oct. 2001.
S. H. Kulkarni, A. N. Srivastava, and D. Sylvester, “A New Algorithm for Improved VDD Assignment in Low Power Dual VDD Systems," in Proceedings of the International Symposium on Low Power Design, pp. 200-205 , 2004.
A. Srivastava, D. Sylvester, and D. Blaauw, “Concurrent Sizing, Vdd and Vth Assignment for Low-Power Design," Proceedings of the Design, Automation and Test in Europe Conference, pp. 107-118, 2004.
K. Kim, Ultra Low Power CMOS Design. PhD thesis, Auburn University, ECE Dept., Auburn, AL, May 2011.

## Slide 49: References
K. Kim and V. D. Agrawal, “Dual Voltage Design for Minimum Energy Using Gate Slack,” in Proceedings of the IEEE International Conference on Industrial Technology, pp. 419-424 , Mar. 2011.
K. Usami and M. Horowitz, “Clustered Voltage Scaling Technique for Low-Power Design," in Proceedings of the International Symposium on Low Power Design, pp. 23-26, 1995.
K. Usami, M. Igarashi, F. Minami, T. Ishikawa, M. Kanzawa, M. Ichida, and K. Nogami, “Automated Low-Power Technique Exploiting Multiple Supply Voltages Applied to a Media Processor," IEEE Journal of Solid-State Circuits, vol. 33, no. 3, pp. 463-472, Mar. 1998.
V. Sundararajan and K. K. Parhi, “Synthesis of Low Power CMOS VLSI Circuits Using Dual Supply Voltages," in Proceedings of the 36th Annual Design Automation Conference, pp. 72-75, 1999.
M. Allani and V. D. Agrawal, “Level-Converter Free Dual-Voltage Design of Energy Efficient Circuits Using Gate Slack,” Submitted to Design Automation and Test in Europe Conference, March 12-16, 2012.

## Slide 50
Thank you.