## Slide 1: Introduction to VHDL
Nikhil Garrepalli
Fall 2012
(Refer to the comments if required)

## Slide 2: HDLs in Digital System Design
Model and document digital systems
  Hierarchical models
    System, RTL (Register Transfer Level), gates
  Different levels of abstraction
    Behavior, structure
Verify circuit/system design via simulation
Synthesize circuits from HDL models

## Slide 3: Hardware Description Languages
VHDL = VHSIC Hardware Description Language (VHSIC = Very High Speed Integrated Circuits)
  Developed by DOD from 1983 – based on ADA
  IEEE Standard 1076-1987/1993/200x
  Based on the ADA language
Verilog – created in 1984 by Philip Moorby of Gateway Design Automation (merged with Cadence)
  IEEE Standard 1364-1995/2001/2005
  Based on the C language
  IEEE P1800 “System Verilog” in voting stage & will be merged with 1364

## Slide 4: Anatomy of a VHDL model
“Entity” describes the external view of a design/component
“Architecture” describes the internal behavior/structure of the component
Example:
1-bit full adder
A
B
Cin
Sum
Cout
Full Adder

## Slide 5: Entity Inputs/Outputs
External view comprises input/output signals (“ports”)
A “port” is defined by its signal name, direction and type:
port_name: direction data_type;
  direction:
    in - driven into the entity from an external source
    out - driven from within the entity
    inout - bidirectional – drivers within the entity and external
  data_type: any scalar or aggregate signal type

## Slide 6: IEEE Standard 1164 Data Types
Type std_logic data values:
‘U’, ‘X’ – uninitialized/unknown ‘0’, ‘1’ – strongly-driven 0/1 ‘L’, ‘H’ – weakly-driven 0/1 (resistive) ‘Z’, ‘W’ - strong/weak “floating” ‘-’ - don’t care
Type std_logic_vector is array of std_logic
Include package: library IEEE; use IEEE.std_logic_1164.all;

## Slide 7: Entity format
ENTITY entity_name IS
GENERIC (optional) (generic_name: type :=default_value;
…
generic_name: mode signal_type);
PORT (signal_name: mode signal_type;
…
signal_name: mode signal_type);
END ENTITY entity_name;

## Slide 8: Full-Adder Adds Three Bits
a
b
XOR
AND
XOR
AND
OR
c_in
sum
c_out
FA
h_s
(a, b)
c_o
(a, b)
h_s
(h_s(a, b), c_in)
c_o
(h_s(a, b), c_in)
HA
HA

## Slide 9: Entity example (1-Bit Full Adder)
ENTITY Full_adder IS
PORT ( -- I/O ports
a: IN STD_LOGIC; -- a input
b: IN STD_LOGIC; -- b input
cin: IN STD_LOGIC; -- carry input
sum: OUT STD_LOGIC; -- sum output
cout: OUT STD_LOGIC); -- carry output
END Full_adder ;
A
B
Cin
Sum
Cout
Full Adder

## Slide 10: Architecture format
ARCHITECTURE architecture_name OF entity_name IS
  -- data type definitions (ie, states, arrays, etc.)
  -- internal signal declarations
  -- component declarations
  -- function and procedure declarations
BEGIN
  -- behavior of the model is described here using:
    -- component instantiations
    -- concurrent statements
    -- processes
END ARCHITECTURE architecture_name;

## Slide 11: Dataflow architecture example
ARCHITECTURE dataflow OF Full_adder IS
BEGIN
sum <= a xor b xor cin;
cout <= (a and b) or (a and cin) or
(b and cin);
END dataflow;

## Slide 12: Structural architecture example
ARCHITECTURE structure OF Full_adder IS
COMPONENT xor IS -- declare component to be used
PORT (x,y: IN STD_LOGIC;
z: OUT STD_LOGIC);
END COMPONENT xor;
COMPONENT or IS -- declare component to be used
PORT (x,y: IN STD_LOGIC;
z: OUT STD_LOGIC);
END COMPONENT or;
COMPONENT and IS -- declare component to be used
PORT (x,y,z: IN STD_LOGIC;
p: OUT STD_LOGIC);
END COMPONENT xor;
SIGNAL x1,x2,x3,x4: STD_LOGIC; -- signal internal to this component
BEGIN
G1: xor PORT MAP (a, b, x1); -- instantiate 1st xor gate
G2: xor PORT MAP (x1, Cin, Sum); -- instantiate 2nd xor gate
G3: or PORT MAP (a, b, x2); -- instantiate 1st or gate
G4: or PORT MAP (a, Cin, x3); -- instantiate 2nd or gate
G5: or PORT MAP (b, Cin, x4); -- instantiate 3rd or gate
G6: and PORT MAP (x2, x3, x4, Cout); -- instantiate and gate
END structure;
Full-adder

## Slide 13: Alternative structural architecture example
ARCHITECTURE structural OF Full_adder IS COMPONENT half_adder PORT(a,b : IN STD_LOGIC; sum, carry : OUT STD_LOGIC); END COMPONENT; COMPONENT or_2 PORT(a,b : IN STD_LOGIC; c : OUT STD_LOGIC); END COMPONENT; SIGNAL int1, int2, int3 : STD_LOGIC; BEGIN H1: half_adder port map(a=>A, b=>B, sum=>int1, carry=>int3); H2: half_adder port map(a=>s1, b=>C_in, sum=>sum, carry=>s2); O1: or_2 port map(a=> int2, b=>int3, c=>C_out);
END structural;
ENTITY half_adder IS PORT (a,b : IN STD_LOGIC ; sum,carry : OUT STD_LOGIC); END half_adder; ARCHITECTURE dataflow OF half_adder IS BEGIN sum<= a xor b; carry <= a and b; END dataflow;
ENTITY or_2 IS PORT (a,b : IN STD_LOGIC ; c : OUT STD_LOGIC); END or_2; ARCHITECTURE dataflow OF or_2 IS BEGIN c<= a or b; END dataflow;
Each Half-adder
Full-adder
Full-adder

## Slide 14: Extending full-adder circuit to multiple-bit adition
library ieee;
use ieee.std_logic_1164.all;
ENTITY adder_4bit IS
PORT (a, b: IN STD_LOGIC_VECTOR(3 DOWNTO 0);
Cin : IN STD_LOGIC;
sum: OUT STD_LOGIC_VECTOR (3 DOWNTO 0);
Cout: OUT STD_LOGIC);
END adder_4bit;
ARCHITECTURE structural OF adder_4bit IS
SIGNAL c: STD_LOGIC_VECTOR (4 DOWNTO 0);
COMPONENT Full_adder
PORT(a, b, c: IN STD_LOGIC;
sum, carry: OUT STD_LOGIC);
END COMPONENT;
BEGIN
FA0: Full_adder
PORT MAP (a(0), b(0), Cin, sum(0), c(1));
FA1: Full_adder
PORT MAP (a(1), b(1), C(1), sum(1), c(2));
FA2: Full_adder
PORT MAP (a(2), b(2), C(2), sum(2), c(3));
FA3: Full_adder
PORT MAP (a(3), b(3), C(3), sum(3), c(4));
Cout <= c(4);
END structural;

## Slide 15: Behavioral architecture example
ARCHITECTURE behavioral OF Full_adder IS
BEGIN
Sum: PROCESS(a, b, cin)
BEGIN
sum <= a xor b xor cin;
END PROCESS Sum;
Carry: PROCESS(a, b, cin)
BEGIN
cout <= (a and b) or (a and cin) or (b and cin);
END PROCESS Carry;
END behavioral;
ARCHITECTURE behavioral OF Full_adder IS
BEGIN
PROCESS(a, b, cin)
BEGIN
sum <= a xor b xor cin;
cout <= (a and b) or (a and cin) or (b and cin);
END PROCESS;
END behavioral;

## Slide 16: VHDL “Process” Construct
Allows conventional programming language methods to describe circuit behavior
Supported language constructs (“sequential statements”) – only allowed within a process:
  variable assignment
  if-then-else (elsif)
  case statement
  while (condition) loop
  for (range) loop

## Slide 17: Process Format
[label:] process (sensitivity list)
declarations
begin
sequential statements
end process;
Process statements executed once at start of simulation
Process halts at “end” until an event occurs on a signal in the “sensitivity list”

## Slide 18: Using a “process” to model sequential behavior
ENTITY dff IS
PORT (d,clk: IN STD_LOGIC;
q: OUT STD_LOGIC);
END dff;
ARCHITECTURE behavioral OF dff IS
BEGIN
PROCESS(clk) -- “process sensitivity list”
BEGIN
IF (clk’event and clk=‘1’) THEN
q <= d AFTER 1 ns;
END IF;
END PROCESS;
END behavioral;
Process statements executed sequentially (sequential statements)
clk’event is an attribute of signal clk which is TRUE if an event has occurred on clk at the current simulation time
D Q
CLK

## Slide 19: Alternative to sensitivity list
ENTITY dff IS
PORT (d,clk: IN STD_LOGIC;
q: OUT STD_LOGIC);
END dff;
ARCHITECTURE behavioral OF dff IS
BEGIN
PROCESS -- no “sensitivity list”
BEGIN
WAIT ON clk; -- suspend process until event on clk
IF (clk=‘1’) THEN
q <= d AFTER 1 ns;
END IF;
END PROCESS;
END behavioral;
Other “wait” formats:
WAIT UNTIL (clk’event and clk=‘1’) WAIT FOR 20 ns;
Process executes endlessly if no sensitivity list or wait statement!
D Q
CLK

## Slide 20: Sequential statements in process
if-then-elsif-else statement if condition then (... sequence of statements...) elsif condition then (... sequence of statements...) else (... sequence of statements...) end if;
case statement case expression is when choices => sequence of statements when choices => sequence of statements ... when others => sequence of statements end case;

## Slide 21: Sequential statements in process
while loop [label:] while condition loop ... sequence of statements ... end loop [label];
for loop [label:] for loop_variable in range loop ... sequence of statements... end loop [label];

## Slide 22: Behavioral architecture example using conditional statements
ARCHITECTURE functional OF Full_adder IS BEGIN PROCESS(A,B,Cin) BEGIN If (Cin = '0' and A = '0' and B = '0' ) then sum<= '0'; Cout <= '0'; elsif(Cin = '0' and A = '0' and B = '1') then sum <= '1' ; Cout <= '0'; elsif(Cin = '0' and A = '1' and B = '0' ) then sum <= '1' ; Cout <= '0'; elsif(Cin = '0' and A = '1' and B = '1' ) then sum<= '0'; Cout <= '1';
  elsif(Cin = '1' and A = '0' and B = '0' ) then sum <= '1' ; Cout <= '0'; elsif(Cin = '1' and A = '0' and B = '1' ) then sum<= '0'; Cout <= '1'; elsif(Cin = '1' and A = '1' and B = '0' ) then sum<= '0'; Cout <= '1'; elsif(Cin = '1' and A = '1' and B = '1' ) then sum <= '1' ; Cout <= '1'; else sum <= 'X' ; Cout <= 'X'; end if;
  END PROCESS;
  END functional;

## Slide 23: Sequential architecture example
ENTITY counter_4bit IS
PORT(Ld, Clr, Clk: IN STD_LOGIC;
D: IN STD_LOGIC_VECTOR (3 DOWNTO 0);
Cout: OUT STD_LOGIC;
Qout: OUT STD_LOGIC_VECTOR (3 DOWNTO 0));
END counter_4bit;
ARCHITECTURE behavioral OF counter_4bit IS
SIGNAL Q: STD_LOGIC_VECTOR(3 DOWNTO 0);
BEGIN
Qout <= Q;
Cout <= Q(3) and Q(2) and Q(1) and Q(0);
PROCESS(Clk)
BEGIN
IF Clk'event and Clk = '1' THEN
IF Clr = '0' THEN
Q <= "0000";
ELSIF Ld = '0' THEN
Q <= D;
ELSE
Q <= Q + 1;
END IF;
END IF;
END PROCESS;
END behavioral;

## Slide 24: References
VHDL mini-reference on Prof. Nelson’s website
  http://www.eng.auburn.edu/department/ee/mgc/vhdl.html
VHDL resources on Prof. Stroud’s website
  http://www.eng.auburn.edu/~strouce/elec4200.html
VHDL resources on Prof. Agrawal’s website
  http://www.eng.auburn.edu/~agrawvd/COURSE/E6200_Fall10/course.html
http://esd.cs.ucr.edu/labs/tutorial/
http://www.seas.upenn.edu/~ese201/vhdl/vhdl_primer.html#_Toc526061344
http://www.vhdl.org/
http://www.doulos.com/knowhow/vhdl_designers_guide/
http://www.altera.com/support/examples/vhdl/vhdl.html
http://www.vhdl-online.de/tutorial/
http://www.people.vcu.edu/~rhklenke/tutorials/vhdl/modules/m12_23/sld006.htm
http://www.doc.ic.ac.uk/~ih/teaching/lectures/comparch/logic/adder/

## Slide 25: Using Modelsim
Modelsim PE (Student Edition) can be downloaded from
http://model.com/content/modelsim-pe-student-edition-hdl-simulation?quicktabs_4=1#quicktabs-4
Modelsim is installed on the Windows7 platform in Lab 310, Broun Hall.

## Slide 26: Using Modelsim

## Slide 27: Using Modelsim

## Slide 28: Using Modelsim

## Slide 29: Using Modelsim

## Slide 30: Using Modelsim

## Slide 31: Using Modelsim

## Slide 32: Using Modelsim

## Slide 33: Using Modelsim

## Slide 34: Using Modelsim

## Slide 35: Using Modelsim

## Slide 36: Using Modelsim

## Slide 37: Using Modelsim

## Slide 38: Using Modelsim

## Slide 39: Using Modelsim