ELEC 2200-002 Digital Logic Circuits 
Fall 2015

Homework 4 Problems

Assigned 10/29/15, due 11/6/15

Problem 1: A four-variable Boolean function is expressed as a sum of three product terms (or cubes):

- Use consensus and absorption theorems to transform the right hand side to a sum of prime implicants (PI).

- Using a Karnaugh map, identify all essential prime implicants (EPI). Express the function as a sum consisting only of PIs.

# Problem 2: Using a Karnaugh map, find the minimum sum of products (MSOP) form for the four-variable Boolean function:

# F(A,B,C,D) = ( m(7, 9, 10, 11, 13) + d(0, 5, 6, 14, 15)

# Problem 3: Using the consensus theorem and absorption theorem, find all prime implicants (PI) of the function,

# Show that there are no essential prime implicants (EPI). Find the MSOP form. Illustrate all PI’s on a Karnaugh map.

# Problem 4: Use the Quine-McCluskey method to minimize the Boolean function,

# F(A,B,C,D) = ( m(1, 6, 10, 12, 15) + ( d(5, 7, 11, 13)

# Show the final result on a Karnaugh map.