## Slide 1: PowerPC
Computer Architecture and Design Fall 2009
Indraneil Gokhale

## Slide 2: Introduction
POWER is a RISC instruction set architecture designed by IBM. The name is a ackronym for Performance Optimization With Enhanced RISC
Created by the 1991 Apple-IBM-Motorola alliance, known as AIM.
PowerPC is largely based on IBM's POWER architecture, and retains a high level of compatibility with it; the architectures have remained close enough that the same programs and operating systems will run on both if some care is taken in preparation.
32-bit and 64-bit PowerPC processors have been a favorite of embedded computer designers. To keep costs low on high-volume competitive products, the CPU core is usually bundled into a system-on-chip (SOC) integrated circuit.

## Slide 3: RISC VS CISC
CISC
MUL 2:3,5:2
RISC
LOAD A, 2:3 LOAD B, 5:2 PROD A, B STORE 2:3, A
RISC – relatively few number of Pipelined Instructions to achieve a high throughput on each clock pulse.

## Slide 4: AIM Contributions
IBM - Record Breaking RISC Architecture
APPLE - Pink Operating System to Run on the POWERPC
MOTOROLA – Chip Designers and Submicron Chip Fabrication Plant.

## Slide 5: What They Gained !!!
IBM - merchant semiconductor market they were looking for.
APPLE - got to use one of the most powerful RISC CPUs on the market, and massive press buzz due to IBM's name.
MOTOROLA - got an up-to-date RISC chip, and help with design methodology from IBM.
(Motorola already had its own RISC design in the form of the 88000 which was doing poorly in the market)

## Slide 6: PowerPC and Power Architecture
The PowerPC architecture is a modified version of the POWER architecture.
The PowerPC architecture added:
Single-precision floating point instructions.
General register-to-register multiply and divide instructions.
Removed some POWER features such as the specialized multiply and divide instructions using the MQ register.
It also added a 64-bit version of the architecture.
PowerPC 600 family, PowerPC 700 family, PowerPC 900 family, PowerPC 400.

## Slide 7: Current Status
PowerPC e200 - 32 bit power architecture microprocessor - speed ranging up to 600 MHz - ideal for embedded applications.
PowerPC e300 – similar to e200 with an increase in speed upto 667 MHz.
PowerPC e600 – speed upto 2 Ghz – ideal for high performance routing and telecommunications applications.
POWER5 – IBM – dual core μP
POWER6 – IBM – Dual core μP - A notable difference from POWER5 is that the POWER6 executes instructions in-order instead of out-of-order
PowerPC G3 - Apple Macintosh computers such as the PowerBook G3, the multicolored iMacs, iBooks and several desktops, including both the Beige and Blue and White Power Macintosh G3s.
PowerPC G4 - is a designation used by Apple Computer to describe a fourth generation of 32-bit PowerPC microprocessors.
PowerPC G5 - 64-bit Power Architecture processors
Cell is a microprocessor architecture jointly developed by Sony Computer Entertainment, Toshiba, and IBM – PS3 game console
Xenon - based on IBM’s PowerPC ISA – XBOX 360 game console.
Broadway – based on IBM’s PowerPC ISA – Nintendo Wii gaming console
Blue Gene/L - dual core PowerPC 440, 700 MHz, 2004
Blue Gene/P - quad core PowerPC 450, 850 MHz, 2007

## Slide 8: MPC601 Architecture
Fixed length 32-bit wide Instructions
3 parallel execution units
Branch Processing Unit
Interger Unit
Floating Point Unit
Instructions are dispatched to the different execution units via an Instruction Unit, which can queue up to 8 instructions and has a dedicated adder for prefetching.

## Slide 9: PowerPC 601 Architecture

## Slide 10: Pipeline Structure

## Slide 11: Instruction Queue and Dispatch Logic
It is Fed by eight-word bus from the cache.
During each cycle, the dispatch logic considers the bottom four entries of the instruction queue and dispatches up to three instructions.

## Slide 12: Future Technologies:
POWER7 - currently under development at about a dozen IBM sites including IBM's Rochester, Austin and Böblingen laboratories as of April 2006.
The POWER7 is the successor to POWER6 and will be released in mid-2010.
PowerPC e700 or NG-64 (Next Generation 64-bit) a line of future high performance 64-bit embedded RISC-processor cores built using Power Architecture technology designed by Freescale.
TITAN – 32 bit Power Architecture -based microprocessors designed by Applied Micro Circuits Corporation (AMCC)

## Slide 13: References
A. Marsala and B. Kanawati, “PowerPC Processors”, Proc. 26th IEEE Southeastern Symp. System Theory, 20-22 March, 1994, pp. 550-556.
Michael K. Becker, Michael S. Allen, Charles R. Moore, John S. Muhich, David P. Tuttle, "The Power PC 601 Microprocessor," IEEE Micro, vol. 13, no. 5, pp. 54-68, Sep/Oct, 1993
http://en.wikipedia.org/wiki/PowerPC
http://www.experiencefestival.com/a/powerpc%20-%20history/id/5389870