## Slide 1: Introduction to writing a Test Bench in HDL
Mridula Allani

## Slide 2: What is A Test Bench?
Test Bench is a program that verifies the functional correctness of the hardware design.
The test bench program checks whether the hardware model does what it is supposed to do and is not doing what it is not supposed to do.

## Slide 3: Main Functions of a Test Bench
Generate stimulus for testing the hardware block.
Apply the stimulus.
Compare the generated outputs against the expected outputs.
Generating
Input
Stimuli
Design Under Test (DUT)
Comparing
Generated Outputs and Expected Outputs

## Slide 4: Generating Stimulus Vectors
Vectors can be generated within the test bench program or generated elsewhere and supplied to the test bench program as an input file.
Vectors can also be stored in a table within the test bench program.

## Slide 5: Typical VHDL Test Bench
entity test_bench is
end;
architecture tb_behavior of test_bench is
component design_under_test
port ( list-of-ports-their-types-and-modes);
end component;
Local-signal-declarations;
begin
CLOCK: process
begin
clock <= '0'; wait for t ns;
clock <= '1'; wait for t ns;
end process;
Generate-stimulus-vectors-using-behavioral-constructs;
Apply-to-entity-under-test;
DUT: design_under_test port map ( port-associations );
Monitor-output-values-and-compare-with-expected-values;
if (no errors)
report "Testbench completed!"
severity note;
else
report "Something wrong!"
severity error;
end if;
end tb_behavior;

## Slide 6: Defining a Vector Table in VHDL
Example,
constant no_of_bits: INTEGER := 4;
constant no_of_vectors: INTEGER := 5;
type table_type is array (1 to no_of_vectors) of
my_vector(1 to no_of_bits);
constant vector_period: time := 100 ns;
constant input_vectors: table_type :=
("1001", "1000", "0010", "0000", "0110");
signal inputs: my_vector(1 to no_of_bits);
signal a, b, c: my;
signal d: my_vector(0 to 1);

## Slide 7: Reading vectors from a ASCII file
Example,
process
  type vec_type is file of my.vector;
  file vec_file: vec_type is in "/usr/example.vec";
    variable length: INTEGER;
  variable in_vector: my_vector(1 to 4);
  begin
    length := 4; - The number of bits to be read.
  while (not ENDFILE(vec_file)) loop
  READ (vec_file, in_vector, length);
  - It is necessary to specify the length of the vector to be read
  - since the file contains values of an unconstrained array type.
    end loop;
end process;

## Slide 8: A Linear VHDL Test Bench
Example,
inputs <= input_vectors(1) after 10 ns,
input_vectors(2) after 25 ns,
input_vectors(3) after 30 ns,
input_vectors(4) after 32 ns,
input_vectors(5) after 40 ns;
a<= inputs(1);
b <= inputs(4);
c<=inputs(1);
d<=inputs(2 to 3);

## Slide 9: Using a ‘generate’ statement
Example,
G1: for J in 1 to no_of_vectors generate
inputs <= input_vectors(J) after (vector_period * J);
end generate G1;
a<= inputs(1);
b <= inputs(4);
c<=inputs(1);
d<=inputs(2 to 3);

## Slide 10: Using Random Numbers in VHDL
uniform(variable seed1, seed2 : inout positive; variable X : out real);
1 <= seed1 <= 2147483562
1 <= seed2 <= 2147483398
Example,
PROCESS
VARIABLE seed1, seed2: positive; -- Seed values for random generator
VARIABLE rand: real; -- Random real-number value in range 0 to 1.0
VARIABLE int_rand: integer; -- Random integer value in range 0..4095
VARIABLE stim: std_logic_vector(31 DOWNTO 0); -- Random 32-bit stimulus
BEGIN
for i in 1 to 1000 loop
UNIFORM(seed1, seed2, rand); -- generate random number
int_rand := INTEGER(TRUNC(rand *256.0)); -- Convert to integer in range of 0 to 255
--, find integer part
stim := std_logic_vector(to_unsigned(int_rand, stim'LENGTH)); -- convert to --std_logic_vector
end loop;

## Slide 11: Libraries needed
use ieee.std_logic_1164.all;
use ieee.std_logic_textio.all; --For file operations
use ieee.numeric_std.all; --For unsigned numbers
use ieee.math_real.all;--For random number generation
use std.textio.all;

## Slide 12: Simple Example in VHDL
library ieee; use ieee.std_logic_1164.all;
use ieee.std_logic_unsigned.all;
use ieee.std_logic_arith.all;
entity counter_TB is -- entity declaration
end counter_TB;
architecture TB of counter_TB is
component counter port( clock: in std_logic; clear: in std_logic; count: in std_logic; Q: out std_logic_vector(1 downto 0) );
end component;
signal T_clock: std_logic;
signal T_clear: std_logic;
signal T_count: std_logic;
signal T_Q: std_logic_vector(1 downto 0);
begin
U_counter: counter port map (T_clock, T_clear, T_count, T_Q);
process
begin
T_clock <= '0'; -- clock cycle is 10 ns wait for 5 ns;
T_clock <= '1'; wait for 5 ns;
end process;
process
variable err_cnt: integer :=0;
begin T_clear <= '1'; -- start counting
T_count <= '1'; wait for 20 ns;
T_clear <= '0'; -- clear output
-- test case 1
wait for 10 ns;
assert (T_Q=1)
report "Failed case 1" severity error;
if (T_Q/=1) then
err_cnt := err_cnt+1; end if;
-- test case 2
wait for 10 ns;
assert (T_Q=2)
report "Failed case 2" severity error;
if (T_Q/=2) then err_cnt := err_cnt+1; end if;
if (err_cnt=0) then
assert false
report "Testbench of Adder completed successfully!" severity note;
else
assert true
report "Something wrong, try again" severity error; end if;
wait;
end process;
end TB;

## Slide 13: Typical Verilog Test Bench
module test_bench ;
reg list_of_inputs_to_DUT;
wire list_of_outputs_to_DUT;
design_under_test
( list-of-inputs-outputs-of-DUT-their-types-and-modes);
initial
begin
Initialize-Generate-stimulus-vectors-using-behavioral-constructs;
end
always
#period clk = ! clk;
initial
begin
$dumpfile (“dump.vcd");
$dumpvars;
end
initial
begin
$display (“variable list with their type specifier”);
$monitor(“variable list with their type specifier”);
end
initial
#simulation_time $finish;
//Rest of testbench code after this line
endmodule

## Slide 14: Defining a Vector Table in Verilog
Example,
no_of_bits = 4;
no_of_vectors = 5;
reg [0 : (no_of_vectors-1)] table[0: (no_of_bits-1)];
vector_period = 100 ns;
table[0] = 4’b1001;
table[1] = 4’b1000;
table[2] = 4’b0010;
table[3] = 4’b0000;
table[4] = 4’b0110 ;

## Slide 15: Reading vectors from a ASCII file
Example,
  vec_file = $fopen("/usr/example.vec“);
  results = $fopen(" /usr/results .dat");
  reg [3:0] my_vector length [0:3] ; //The number of vectors and number of bits to be read for each vector.
  c = $fgetc(file);
  while (c !== `EOF)
  begin
  $readmemh (“vec_file”, length ); //Read hex file content into a memory array.
  $readmemb (“vec_file”, length ); //Read binary file content into a memory array.
  $fdisplay (results, variable list with format specifiers);
  $fmonitor (results, variable list with format specifiers);
  $fclose (results);
  $fclose (vec_file );
  end
end process;

## Slide 16: A Linear Verilog Test Bench
Example,
#10 ns inputs = input_vectors(1);
# 25 ns inputs = input_vectors(2);
# 30 ns inputs = input_vectors(3);
# 32 ns inputs = input_vectors(4);
# 40 ns inputs = input_vectors(5);
a = inputs[1];
b = inputs[4];
c =inputs[1];
d =inputs[2 : 3];

## Slide 17: Using a ‘generate’ statement
Example,
generate
genvar j;
for (j=0; j<= no_of_vectors; j=j+1)
begin
vector_period = (vector_period * j) ;
#vector_period inputs = input_vectors(j); end
endgenerate
a = inputs[1];
b = inputs[4];
c =inputs[1];
d =inputs[2 : 3];

## Slide 18: Using Random Numbers in Verilog
Example 1,
module test ();
integer address; initial begin repeat(5) #1 address = $random;
end initial $monitor("address = %d;",address); endmodule RESULT: //any 32-bit integer
Example 2,
module Tb();
integer add_2, add_3;
reg [31:0] add_1; initial begin repeat(5) begin #1; add_1 = $random % 10; add_2 = {$random} %10 ; add_3 = $unsigned($random) %10 ; end end initial $monitor("add_3 = %d;add_2 = %d;add_1 = %d",add_3,add_2,add_1); endmodule RESULT: add_3 = integers between 0 and 10
add_2 = integers between 0 and 10
add_1 = the result will not be an integer between 0 and 10 because $random also generates some negative 32-bit numbers.
In general,
min + {$random} % (max - min )
will generate random numbers between min and max.

## Slide 19: Simple Example in Verilog
module tb_ripple_adder();
reg [1:0] a, b;
reg carryin;
wire carrout;
wire [1:0] sum;
ripple_adder DUT (.sum(sum), .carryout(carryout), .a(a), .b(b), .carryin(carryin));
initial
begin
//=====VCD====
$dumpfile ("synthesized.dump");
$dumpvars (0, tb_ripple_adder);
//=====initialization ====
a = 2'b00; b = 2'b00;carryin = 0;
//=====vector generation=========
#50 a = 2'b00; b = 2'b01; #50 a = 2'b00; b = 2'b10;
#50 a = 2'b00; b = 2'b11;
end
//=====display=====
always @(a or b or carryin)
$display ("time=%t", $time, "carryin=%b", carryin, "a=%b", a, "b=%b", b, "carryout=%b", carryout, "sum=%b", sum);
//======job control=====
initial
begin
#10001 $finish;
end
endmodule

## Slide 20: References
A VHDL Primer, 3rd Edition, J. Bhaskar
http://testbench.in/
http://www.eng.auburn.edu/~strouce/class/elec4200/TestBench.pdf
http://www.synthworks.com/downloads/ConstrainedRandom_SynthWorks_2009.pdf
http://esd.cs.ucr.edu/labs/tutorial/
http://www.markharvey.info/vhdl/rnd/rnd.html
http://www.questatechnologies.com/VHDLTestbenchGenerator.html
http://www.xilinx.com/itp/xilinx8/books/data/docs/xst/xst0086_10.html