## Slide 1: Formal Verification of Digital Systems
Model Checking
Suraj Sindia
11 April 2012

## Slide 2: What is Model Checking?
Are we checking these kind of models…?
Unfortunately, no!

## Slide 3: Verification of Circuits
Simulation based verification
  Applying a known stimulus to a circuit, and ensuring that all its outputs meet pre-determined performance criteria
    Logic simulation – E.g.: ModelSim
    Timing simulation – E.g.: HSPICE
  Historically most prevalent form of verification
  Time for verification grows exponentially with number of inputs
    For most real designs, needs application of 60-70% of all input vectors to validate a circuit’s functionality
      This implies there is no 100% guarantee that a design is correct!

## Slide 4: Verification of Circuits
Formal verification
  Ensuring that a circuit satisfies (or does not satisfy) all its desired (or undesired) behavior by building a logical formalism – an abstraction – for the circuit being tested
  The behavior being tested for, is also expressed in the same abstract form
  Some examples: equivalence checking, model checking, static timing analysis (most of us are oblivious to the fact that this is a formal scheme for ensuring timing correctness of a circuit)

## Slide 5: Formal Verification of Circuits
Primarily is used in two flavors today –
  Equality checking
    Two implementations of a circuit are formally compared to check if they both are equivalent
      For example: Comparing RTL vs. gate level netlist of a design
      Formality from Synposys
  Model checking
    Some behavior of the circuit is abstracted and the following question is posed:
      “Does the circuit satisfy this behavior?”
      Focus of this and next class

## Slide 6: Inventors of Model Checking
ACM Turing award citation
Joseph Sifakis, CNRS Grenoble, France
E. Allen Emerson, UT Austin

## Slide 7: Abstractions for Model Checking
Linear Temporal Logic (LTL)
Computation Tree Logic (CTL)
In this and next class
  We will learn these two languages
  Use them to specify properties, and verify finite state machines (FSM)

## Slide 8: Propositional Logic - Basics
AND (˄)
OR (˅)
NOT (¬)
IMPLICATION (→)
BI-CONDITIONAL (↔)

## Slide 9: Summary of Truth Tables
p | q | p ∧ q | (p ∨ q) | p → q | p ↔ q
T | T | T | T | T | T
T | F | F | T | F | F
F | T | F | T | T | F
F | F | F | F | T | T

## Slide 10: LTL for Model Checking: Example 1

## Slide 11: LTL for Model Checking: Example 2

## Slide 12: LTL for Equivalence Checking

## Slide 13: Computation Tree Logic (CTL)

## Slide 14: CTL State Operators: Quick Illustration
Fp – p holds in some future state
Gp – p holds globally in future states
p
~p
~p
~p
~p
~p
x
s0
s1
s2
s3
sn
sn+1
sn+2
p
~p
~p
~p
p
p
p
s0
s1
s2
s3
sn
sn+1
sn+2
x
denotes don’t care

## Slide 15: CTL State Operators: Quick Illustration
Xp – p holds in next state
pUq – p holds until q
p
~p
x
s0
s1
s2
x
p
p
p
q
q
x
s0
s1
s2
s3
sn
sn+1
sn+2
x
denotes don’t care

## Slide 16: CTL State Operators: Quick Illustration
pWq – p holds until q
x
p
p
p
pvq
x
s0
s1
s2
s3
sn
sn+1
sn+2
x
denotes don’t care
pvq

## Slide 17: CTL Path Operators
A(arg) – Along all paths starting at state s0 arg is True.
s0
Example: AGp

## Slide 18: CTL Path Operators
E(arg) – Along some path starting at state s0 arg is True.
s0
Example: EGp

## Slide 19: References
Logic in Computer Science – Modelling and Reasoning about Systems
  2nd edition of this book by M. Huth and M. Ryan and published by Cambridge press.
  Covers all the aspects of LTL and CTL, with several nice examples, that we studied over the last two classes.
  Warning: Can be overwhelming in the beginning!
Comprehensive Functional Verification – The Complete Industry Cycle
  Authored by B. Wile, J. C. Goss, W. Roesner and published by Elsevier.
  50% of the book is on simulation based verification and the rest on formal verification.
  Best practices for verifying large and complex industrial designs are discussed.
http://www.design-reuse.com/articles/2287/survey-compares-formal-verification-tools.html
  Survey by Lars Philipson. Gives a list of currently available equivalence checkers and model checkers.

## Slide 20: Doodles Drawn on Paper

## Slide 21: Justifications on a Parse Tree for Checking Equivalence of Two Boolean Functions

## Slide 22: Equivalence Checking

## Slide 23: Parse Tree for a LTL Formulae

## Slide 24: Understanding Implication in LTL

## Slide 25: Verbal Example of an Implication
See that converse is not true.