## Slide 1: Please get some pizza and BBQ

## Slide 2: Evaluating the Digital Fault Coverage of a Mixed-Signal BIST
Alex Lusco

## Slide 3: Thesis Statement
A set of test procedures is evaluated which test the digital portion of a mixed-signal BIST approach using the digital loopback path. To provide context for evaluation, the test procedures are used to create and simulate a set of measurements which test a Selective Signal Analysis (SSA) BIST implementation. In addition to an analysis of the resulting fault coverage, the measurement set is also used to test actual manufactured chips and the results discussed.
Notes: A set of test procedures is evaluated which test the digital portion of a mixed-signal BIST approach using the digital loopback path. By using the digital loopback path no dedicated testing hard such as scan chains is required, minimizing area overhead and performance penalties. A Selective Spectrum Analysis (SSA) BIST implementation is used to provide context and evaluate the fault coverage that can be achieved using these test procedures. In addition to an analysis of the resulting fault coverage, the measurement set is also used to test actual manufactured chips and the results discussed.

## Slide 4: Thesis Outline
Background
  Testing Digital and Mixed-Signal Systems
  Fault Simulation
  The SSA BIST Architecture
Test Preparation
  Conversion to ASL
  Test Development and Verification
Fault Coverage and Results
  Simulation Performance and Results
  Experimental Results
Analysis and Summary

## Slide 5: Fault Simulation
Given a set of test vectors, a circuit can be simulated to determine the fault coverage or percentage of faults detected.
  The fault-free circuit is simulated with a set of test vectors.
  A list of faults is generated based on the circuit design and fault model.
  A fault is emulated in the circuit and then resimulated.
  The output of the faulty circuit is compared to the fault-free output to determine if the fault was detected.
Faults can be detected (D), potentially detected (P), or undetected. They can also be undetectable (X).
  P faults are caused by uninitialized logic values and are typically assumed to be detected 50% of the time (Y=.5).

## Slide 6: Fault Simulation (contd.)
For a large number of faults and/or test vectors simulation time can take prohibitively long.
  Faults can be dropped as soon as the fault is detected by the simulation.
  Faults can be simulated in parallel, usually in batches of 32 or 64.
  Faults can be collapsed; faults which produce identical behavior only need to be simulated once.
  Techniques can be combined to gain further speed up.
AUSIM by Dr. Stroud is the simulator used in this thesis.
With Fault Dropping
With Parallel Simulation
With Both

## Slide 7: Testing of Digital Systems
Digital systems operate at a discrete logic level of '1' or '0'.
There are many different models for describing faults in a digital system. Each having it's own advantages and disadvantages.
In this thesis the gate-level, single, stuck-at fault model is used since it is computationally efficient and reasonably accurate.
  Faults can occur at the gate level on inputs and outputs (IO).
  Any gate IO can be stuck-at logic '0' or stuck-at logic '1'.
  As shown in the figure a fault is denoted by an 'X' over the input or output with the SA abbreviation denoting the fault.
Inputs (AB) | Fault-Free Output (Z) | Faulty Output (Z)
00 | 0 | 0
01 | 0 | 1
10 | 0 | 0
11 | 1 | 1
AND Gate with input stuck-at '1'
X
SA1
A
B
Z

## Slide 8: Testing of Mixed-Signal Systems
Includes both digital and analog components in the same system.
  Signals are usually converted back and forth from the analog to digital domain using both analog-to-digital (ADC) and digital-to-analog (DAC) converters.
  Unlike digital devices, analog components operate in range of acceptable values complicating testing.
    This prevents the exact circuit response from being known during testing.
Traditionally the digital and analog portions of the device are tested separately using different techniques.
  Allows for the use of testing techniques best suited for each sub-system.
Effectively testing the digital components requires them to be isolated from the analog system.

## Slide 9
Typical Mixed-Signal System
Digital System
Analog System
Analog System
Digital System
Digital Inputs
Digital Outputs
Analog Inputs
Analog Outputs
A D C
D A C
Analog Loopback

## Slide 10: Testing Mixed-Signal Systems (contd)
When testing a mixed-signal system from the digital domain test vectors must typically be converted from digital values into analog values, loop through any analog components, then be converted back and read.
Due to the conversion from digital to analog, a range of outputs are acceptable for a given input.
  This lowers the fault coverage as it may mask faults in the digital system.
To efficiently test the digital sub-system a path that does not require conversion to analog is required.

## Slide 11
Testing via the Digital Loopback Path
Digital System
Analog System
Analog System
Digital System
Digital Inputs
Digital Outputs
Analog Inputs
Analog Outputs
A D C
D A C
Analog Loopback
Digital Loopback
Analog Bypass

## Slide 12
Testing the via the Bypass Path
Digital System
Analog System
Analog System
Digital System
Digital Inputs
Digital Outputs
Analog Inputs
Analog Outputs
A D C
D A C
Analog Loopback
Digital Loopback
Analog Bypass

## Slide 13
Testing via the Analog Path
Digital System
Analog System
Analog System
Digital System
Digital Inputs
Digital Outputs
Analog Inputs
Analog Outputs
A D C
D A C
Analog Loopback
Digital Loopback
Analog Bypass
Notes: * Additional paths may be added to further partition analog path

## Slide 14: Selective-Spectrum Analysis (SSA) BIST
SSA tests analog circuitry by measuring certain analog characteristics of an analog system at a specific frequency and ensuring it falls within an expected good range.
  Requires significantly less area and power than the full Fast-Fourier Transform (FFT) approach.
The SSA BIST consists of a several major components:
  Direct-Digital Synthesis (DDS) frequency generator which functions as the TPG.
  Two Multiplier-Accumulator based ORAs.
  Calculation Circuit to condition output data.
  Test Controller and Serial-Peripheral (SPI) interface.
Accuracy of SSA is a function of accumulation time:
  More time spent accumulating, the better the accuracy.
  If accumulation is stopped at certain points in time then the accuracy v. time trade off can be minimized.

## Slide 15
SSA BIST Architecture

## Slide 16: Direct-Digital Synthesis (DDS)
Generates sine and cosine signals used to stimulate the analog components as well as reference tones used in the ORA.
Tones are generated based on frequency words and the formula below where n=16 for 16-bit frequency words (FW).
The frequency resolution of the DDS is dependent on the number of bits in the frequency words and the clock speed.
As an example when using 16-bit frequency words at 50MHz. FW 0x100 produces a frequency of ~19.5Khz and the system frequency resolution is ~760Hz.
Phase Accumulator
Phase Truncator
Sin/Cos
LUT
DAC
n
n
p
d
Fw
Fout
Notes: 0x100 = 19.5k Hz @ 50MHz, resolution is 762Hz @ 50MHz

## Slide 17: MAC based ORAs
Two multiplier-accumulators accumulate the in-phase and out-of-phase frequency response of the analog DUT.
Accumulation will introduce errors due to AC frequency components unless accumulation is stopped at an integer multiple period (IMP) of the measured frequencies.
Magnitude and phase can be calculated using the two formulas below where DC1 and DC2 represents the in-phase and out-of-phase frequency accumulations.
DC1
DC2
Output
Fsin
Fcos
Multiplier-Accumulator ORA

## Slide 18: Integer Multiple Period Accumulation Time
By stopping the accumulation at an IMP of the measured frequencies the AC errors will cancel out and the result will be very accurate.
  The time in seconds to accumulate is calculated where f is the frequency of interest.
Using this method the test time is a direct function of the frequency words being generated and can be controlled.
In the case of multiple frequencies being generated (f1 and f2) or the case where multiple frequencies are being generated and a third frequency is being measured (f1, f2, and f3), the IMP is the least common multiple of all frequency periods.
Notes: Simplified, really it’s a function of the phase accumulator too.

## Slide 19: Calculation Circuitry
Uses CORDIC algorithm to convert DC1 and DC2 accumulator values to magnitude and phase values.
In conjunction with the test controller the SSA BIST can measure important analog characteristics which require multiple individual measurements to be performed.
  Linearity of the system.
  Multi-point frequency sweep.
  Signal-to-Noise (SNR) ratio of the system.
  Noise-Figure (NF) of the system.
All calculations are performed in the logarithmic domain to simplify the calculation circuitry and results are in decibels (dB).
Calculations are not performed using floating point and results are expected to be within a dB of the real result.
All output (and input) must be read and written through the SPI.

## Slide 20
Signal-to-Noise Ratio
F1
SNR
Frequency Sweep
2F1-F2
F1
F2
2F2-F1
Linearity
ΔP
Calculation Circuit Measurement Diagrams

## Slide 21
Original Calculation Circuit

## Slide 22: Thesis Outline
Background
  Testing Digital and Mixed-Signal Systems
  Fault Simulation
  The SSA BIST Architecture
Test Preparation
  Conversion to ASL
  Test Development and Verification
Fault Coverage and Results
  Simulation Performance and Results
  Experimental Results
Analysis and Summary

## Slide 23: Conversion to ASL from Verilog
Production circuits are often written in a high level design language such as Verilog or VHDL.
AUSIM fault simulator requires an ASL netlist.
To simplify simulation of complex circuits a converter was written which converts a Verilog netlist to ASL.
  Conversion can be performed at any stage of development: pre or post-layout.
  Has been used to successfully convert and simulate ISCAS'89 for bridging faults (faults which occur between wires).
Written in C#, ~800 lines of (poorly written) code. Took approximately 1 week to develop, and an additional 1 week to verify and fix several edge cases.
Converted circuits can be behaviorally verified against ModelSIM simulations.

## Slide 24: ASL Conversion

## Slide 25: The Test Procedures
Goal is to determine how high of a fault coverage can be achieved by using the SSA BIST to test itself via the digital loopback path.
  Convert the SSA BIST to the ASL format for simulation.
  Verify the correctness of the converted circuit.
  Develop an initial set of measurements to function as test vectors.
  Simulate circuit to determine fault coverage.
  Analyze results and determine if changes to test vector set need to be made.
  Re-simulate new test vectors until fault coverage is sufficient.
  Verify experimentally.

## Slide 26: Test Development Process
Develop New Test Vectors
Perform Simulations
Make Modifications to Test Vectors
Analyze Results

## Slide 27: Initial Test Development
Initial measurement set was developed based on underlying understanding of SSA BIST architecture.
Simple measurements of each type were developed in order to exercise as many sub-systems of the SSA BIST as possible.
Each measurement requires developing the correct SPI words to send to the SSA BIST test controller, and calculating the correct number of clock cycles to simulate the measurement (based on the IMP calculation discussed previously).
After several iterations a total of six measurements were developed and simulated.

## Slide 28
Type | FW1 | FW2 | FW3 | FW4 | TC Word | Sample | Clock Cycles
SNR | 1200 | 1400 | 600 | 200 | 13CC | 513 | 103000
Long Frequency Response | 101 | 101 | 102 | 33 | 0D24 | 0 | 34500
Frequency Sweep | 1000 | 1500 | 100 | 100 | 0CA4 | 513 | 131500
Linearity | 3000 | 5000 | 800 | 0 | 070C | 0 | 1050
Short Frequency Response | 4000 | 6000 | 2000 | 0 | 07A0 | 0 | 900
Noise Figure | 0CFC | 0AFC | 10FC | 7CCC | 1B60 | 2 | 91601
Total Test Vectors: 725,102 |  |  |  | Total Clock Cycles: 362,501 |  |  | 
Simulated Measurement Set

## Slide 29: Thesis Outline
Background
  Testing Digital and Mixed-Signal Systems
  Fault Simulation
  The SSA BIST Architecture
Test Preparation
  Conversion to ASL
  Test Development and Verification
Fault Coverage and Results
  Simulation Performance and Results
  Experimental Results
Analysis and Summary

## Slide 30: Simulation Time
Due to the number of faults in the SSA BIST (approximately 40K collapsed faults), the simulation time required would be too long to facilitate rapid simulation of some of the longer measurements.
  The longest simulation (a combined simulation of all measurements) would take 6400 hours or ~9 months!
To greatly decrease the simulation time the Auburn University High-Performance Computing Cluster (HPCC) was used to perform a large number of simulations in parallel.
  Each parallel simulation simulated a much lower number of faults, approximately 350 faults each.
The graph on the next slide shows the approximate CPU time required in hours compared to the actual time required for simulation (Wall Time).

## Slide 31
Simulation Time in Hours vs CPU Time Required
Chart: CPU Time vs Wall Time
| Combined | SNR | FR | Sweep | IP3 | FR | NF
CPU Time | 6422 | 2018 | 12.5 | 3450 | 8.5 | 609 | 2544
Wall Time | 74 | 20 | 1 | 28 | 1 | 9 | 21.7

## Slide 32
The Fault Coverage of the Simulated Measurement Set
Chart: Fault Coverage Results
| NF | SNR | Long FR | Short FR | Sweep | IP3
Individual Fault Coverage | 31011 | 30572 | 28316 | 23817 | 28423 | 24996
Cumulative Fault Coverage % | 0.7856 | 0.8512 | 0.86931 | 0.87723 | 0.88186 | 0.88508

## Slide 33: Fault Coverage Analysis
An overall fault coverage achieved was 88.64%.
  This fault coverage was lower than expected.
After analysis several sub-systems of the BIST were shown to have an unexpectedly low fault coverage.
Subsystem | Total Faults | Coverage
DDS | 4995 | 99.7%
Fullswing Power | 438 | 70.09%
Calculation Circuit | 11621 | 81.06%
ORA Accumulators | 10608 | 98.37%
Reference CORDIC | 3977 | 95.22%
Spur Calibration | 660 | 71.06%
Test Controller | 1829 | 85.27%
SPI Interface | 4259 | 81.71%

## Slide 34: Coverage Improvements
In an effort to improve the fault coverage, modifications we're made to the SSA BIST to increase the testability of the circuit.
Modifications made include:
  Ability to disable certain output normalization circuitry.
  Ability to attenuate the magnitude of the DDS generated signal.
  Ability to clip the DDS signal so that noise can be introduced into the digital loopback path.
  Allow the testing of included preset circuitry.
  Expose internal registers to the SPI for increased testability.
Four additional measurements were developed to take advantage of the newly implement circuitry.

## Slide 35: Fault Coverage Results and Analysis
A new measurement set consisting of 10 measurements was re-simulated resulting in an increase in fault coverage to 89.5%.
  Unfortunately this is a less than a 1% increase, and not very significant.
One factor contributing to the low fault coverage is the inability to test certain portions of the BIST circuitry while using the digital loopback path.
It is likely that with additional iterations on the measurement set some improvement in fault coverage could be achieved.
Lastly some components of the SSA BIST may need to be redesigned for improved testability.
  When the SPI circuitry is removed the fault coverage of the BIST improves to 91.5%

## Slide 36: Experimental Verification
The initial six measurements were used to experimentally verify a tape-out of the SSA BIST chips.
The six measurements developed require approximately 400,000 clock cycles to run.
  At an 80MHz system clock speed this requires around 10ms.
A number of chips did not produce the correct output, failing the tests and proving to be faulty.
  In at least one case the location of the fault causing a chip to fail was diagnosed based on an analysis of the invalid BIST results.
The successful use of this test procedure proves that it is an efficient and viable method for chip verification and in some cases fault diagnosis.

## Slide 37: Thesis Outline
Background
  Testing Digital and Mixed-Signal Systems
  Fault Simulation
  The SSA BIST Architecture
Test Preparation
  Conversion to ASL
  Test Development and Verification
Fault Coverage and Results
  Simulation Performance and Results
  Experimental Results
Analysis and Summary

## Slide 38: Analysis and Summary
Some difficulties were encountered when using this approach to a mixed-signal BIST approach.
There is no automated tool to develop the test vector set. Development requires some level of trial and error and time to iterate so that a sufficiently high fault coverage can be achieved.
Can be difficult to achieve the highest levels of fault coverage (>95%) without the addition of some dedicated testing hardware.
Certain portions of the BIST circuitry will be untestable.
  External paths and components, such as the bypass and analog loopback paths may prove especially difficult.
  Due to untestable components, additional test techniques may be required to fully test the circuit.

## Slide 39: Analysis and Summary (contd.)
Even though a fault coverage of 88.6% was lower than expected -- a fault coverage of almost 90% still was achieved.
  Compared to partial scan (900 FFs) which increased the chip area by almost 11% area and achieved only 62% coverage using pseudo-random vectors.
  Test procedure is circuit agnostic and can be used to test a number of similar mixed-signal approaches.
  It requires only a Verilog netlist and a digital loopback path.
  It reuses test circuitry already meant to test the analog components keeping area down.
Since no dedicated circuitry is required, testing can occur at system speed and without costly area increases.
Furthermore it can also be performed at any stage of the circuit's lifetime including design, manufacturing, and during system operation.