## Slide 1: Retiming Scan Circuit To Eliminate Timing Penalty
Ozgur Sinanoglu
NYU - AD
Vishwani D. Agrawal
Auburn University
Notes: The slide guide is available in the following file:
slidesV10.1.ppt: PowerPoint, version 2003 format.

## Slide 2
Scan Insertion
Sequential
Circuit
Flip-flops converted to
fully accessible scan cells
Bring the circuit to any state
Observe the state any time
Scan cells controlled and observed through shift operations
Combinational
Circuit
MUX
MUX
MUX
MUX
MUX
Flip-flops
Sequential test generation
Combinational
Notes: To deal with the sequentiality problem, one widely utilized DfT approach scan insertion. With the late addition of Intel, any chip design company is utilizing scan insertion today. The idea is adding some multiplexer logic to convert registers into fully accessible scan elements during test so that with shift operations desired stimulus can be loaded into the registers while their content can be unloaded for observation. However,still the number of possible patterns is exponential in the number of registers, which approaches one M today.

## Slide 3
Automatic
Test
Equipment
Scan Based Test
Circuit
Under
Test
Automatic
Test
Equipment
  Test application:
  Loading stimulus
  Capturing response
  Unloading response
MUX
D
Q
Scan_en
clk
S_in
F_in
S_out
F_out
Scan MUX
Scan cell
Can select:
Functional input
Scan input
Notes: Testers typically have multiple channels; however, the more the channels, the costlier. But multitude of channels enables multiple scan chains. Instead of having one long scan chain, we break it into multiple shorter scan chains, so the load/unload operations take fewer cycles.

## Slide 4
Scan Multiplexer
Scan delay = (Fanout + MUX) delay on functional paths
 performance degradation (slower chip!)
MUX
D
Q
Scan_en
clk
S_in
F_in
S_out
Scan multiplexers enable full access to registers during test
  Sequential test generation → combinational test generation
  Test generation complexity, test quality, debugging benefits
F_out
Scan MUX
Scan cell
MUX
D
Q
Combo path
Remedy: Partial Scan?
Test generation complexity!
Notes: As designs are getting more complex and new defect types are emerging due to reduced feature sizes, test will become only more challenging and the answer is modular testing due to all the benefits it offers.

## Slide 5
D
Q
S_in
F_in
S_out
F_out
original
D
Q
Scan_en
shadow
MUX
MUX
Sel_shadow
After transformation
Earlier Work: Scan Cell Transformation
Move the scan MUX off the critical path
  Additionally, 1 FF and 1 MUX inserted per transformation
  Transformation applied on only critical path sinks
    MUX delay moved elsewhere
shorter
longer
D
Q
Scan_en
S_in
F_in
S_out
F_out
original
MUX
Before transformation
Sinanoglu, “Eliminating Performance Penalty of Scan,” VLSI Design 2012
Notes: As designs are getting more complex and new defect types are emerging due to reduced feature sizes, test will become only more challenging and the answer is modular testing due to all the benefits it offers.

## Slide 6
D
Q
S_in
F_in
S_out
F_out
original
D
Q
Scan_en
shadow
MUX
MUX
Sel_shadow
After transformation
Earlier Work: Scan Cell Transformation
Scan penalty:
  MUX-delay + fanout-delay
Performance saving by this approach (best case):
  MUX-delay - fanout-delay (not entire scan penalty)
shorter
longer
D
Q
Scan_en
S_in
F_in
S_out
F_out
original
MUX
Before transformation
Sinanoglu, “Eliminating Performance Penalty of Scan,” VLSI Design 2012
Notes: As designs are getting more complex and new defect types are emerging due to reduced feature sizes, test will become only more challenging and the answer is modular testing due to all the benefits it offers.

## Slide 7
Scan Operations with Transformed Cells
D
Q
original
D
Q
shadow
D
Q
original
D
Q
original
3-bit scan chain fragment; middle cell transformed
Combinational Logic
Scan_en
Sel_shadow
Scan_en
Scan_en
S_in
S_out
CAPTURE: Scan-en = 0 Sel_shadow = 1

## Slide 8
Scan Operations with Transformed Cells
D
Q
original
D
Q
shadow
D
Q
original
D
Q
original
3-bit scan chain fragment; middle cell transformed
Combinational Logic
Scan_en
Sel_shadow
Scan_en
Scan_en
S_in
S_out
FIRST SHIFT: Scan-en = 1 Sel_shadow = 0

## Slide 9
Scan Operations with Transformed Cells
D
Q
original
D
Q
shadow
D
Q
original
D
Q
original
3-bit scan chain fragment; middle cell transformed
Combinational Logic
Scan_en
Sel_shadow
Scan_en
Scan_en
S_in
S_out
OTHER SHIFTS: Scan-en = 1 Sel_shadow = 1

## Slide 10
Scan Operations with Transformed Cells
D
Q
original
D
Q
shadow
D
Q
original
D
Q
original
3-bit scan chain fragment; middle cell transformed
Combinational Logic
Scan_en
Sel_shadow
Scan_en
Scan_en
S_in
S_out
Same scan capabilities  Same test time, coverage, etc.

## Slide 11
Proposed: Retiming Scan Circuit
Combinational
Logic
D
Q
D
Q
Retiming in general:
  Moving FFs across combinational logic
  Functionality of a synchronous circuit unchanged
Combinational
Logic
D
Q
Retiming
Proposed solution:
  Apply retiming across scan multiplexer at the critical path sinks
  Apply retiming across scan fanout at the critical path origins
  Save entire scan penalty
C. E. Leiserson, F. Rose, and J. B. Saxe, “Optimizing Synchronous Circuits by Retiming,” Caltech Conf. on VLSI, 1983

## Slide 12
Scan_en
S_in
F_in
D
Q
Critical path
Proposed: Retiming Scan Circuit
D
Q
S_in
F_in
D
Q
Critical path
D
Q
D
Q
D
Q
Scan_en
Scan_en_del
Select between current func/scan input based on current scan-en
Select between registered func/scan input based on registered scan-en
F_out
S_out

## Slide 13
Scan_en
S_in
F_in
D
Q
Critical path
Proposed: Retiming Scan Circuit
D
Q
S_in
F_in
D
Q
Critical path
D
Q
D
Q
D
Q
Scan_en
Scan_en_del
shared
Scan_en_del
Select between current func/scan input based on current scan-en
Select between registered func/scan input based on registered scan-en
F_out
S_out

## Slide 14
Scan_en
S_in
F_in
D
Q
Critical path
Proposed: Retiming Scan Circuit
D
Q
S_in
F_in
D
Q
Critical path
D
Q
D
Q
D
Q
Scan_en
Scan_en_del
shared
Scan_en_del
Identical functionality
  Both normal & scan modes
MUX delay transferred forward
    Best case saving: MUX delay
F_out
S_out

## Slide 15
Proposed: Retiming Scan Circuit
S_in
F_in
D
Q
Critical path
D
Q
D
Q
D
Q
Scan_en
Scan_en_del
Scan_en_del
Impact on test application (stuck-at):
  Loaded stimulus reflects from shadow FF
  Response captured in original FF
  First shift from original FF
  Subsequent shifts from shadow FF
original
shadow
Scan enable
clock
2
3
4
4
1
F_out
S_out

## Slide 16
Proposed: Retiming Scan Circuit
S_in
F_in
D
Q
Critical path
D
Q
D
Q
D
Q
Scan_en
Scan_en_del
Scan_en_del
Impact on test application (LOC-based):
  Loaded stimulus reflects from shadow FF
  Launch from original FF
  Capture in original FF
  First shift from original FF
  Subsequent shifts from shadow FF
original
shadow
Scan enable
clock
5
5
4
1
2
3
F_out
S_out

## Slide 17
Proposed: Retiming Scan Circuit
S_in
F_in
D
Q
Critical path
D
Q
D
Q
D
Q
Scan_en
Scan_en_del
Scan_en_del
Impact on test application (LOS-based):
  Loaded stimulus reflects from shadow FF
  Shift-based launch from shadow FF
  Capture in original FF
  First shift from original FF
  Subsequent shifts from shadow FF
original
shadow
Scan enable
clock
5
5
4
1
2
3
F_out
S_out

## Slide 18
Proposed: Retiming Scan Circuit
S_in
F_in
D
Q
Critical path
D
Q
D
Q
D
Q
Scan_en
Scan_en_del
Scan_en_del
original
shadow
Same scan capabilities  Same test time, coverage, etc.
F_out
S_out

## Slide 19
Impact on Timing
s6
s9
s7
s4
s10
s8
s12
s13
CP
CP – 1.0∆MUX
CP – 0.7∆MUX
CP – 1.5∆MUX
CP – 0.3∆MUX
CP – 0.8∆MUX
All paths within 2∆MUX delays from critical path shown above
Originally | Critical Path: CP

## Slide 20
Impact on Timing
s6
s9
s7
s4
s10
s8
s12
s13
CP
CP – 1.0∆MUX
CP – 0.7∆MUX
CP – 1.5∆MUX
CP – 0.3∆MUX
CP – 0.8∆MUX
All paths within 2∆MUX delays from critical path shown above
CP – 1.0∆MUX
CP – 1.7∆MUX
CP – 0.5∆MUX
Originally | Critical Path: CP

## Slide 21
Impact on Timing
s6
s7
s4
s10
s8
s12
s13
CP – 1.0∆MUX
CP – 0.3∆MUX
CP – 0.8∆MUX
All paths within 2∆MUX delays from critical path shown above
CP – 1.0∆MUX
CP – 1.7∆MUX
CP – 0.5∆MUX
s9
Originally | Critical Path: CP
Trans. #1 | Critical Path: CP - 0.3∆MUX

## Slide 22
Impact on Timing
s6
s7
s4
s10
s8
s12
s13
CP – 1.0∆MUX
CP – 0.3∆MUX
CP – 0.8∆MUX
All paths within 2∆MUX delays from critical path shown above
CP – 1.0∆MUX
CP – 1.7∆MUX
CP – 0.5∆MUX
s9
CP – 1.3∆MUX
Originally | Critical Path: CP
Trans. #1 | Critical Path: CP - 0.3∆MUX

## Slide 23
Impact on Timing
s6
s7
s4
s8
s12
s13
CP – 1.0∆MUX
CP – 0.8∆MUX
All paths within 2∆MUX delays from critical path shown above
CP – 1.0∆MUX
CP – 1.7∆MUX
CP – 0.5∆MUX
s9
CP – 1.3∆MUX
s10
Originally | Critical Path: CP
Trans. #1 | Critical Path: CP - 0.3∆MUX
Trans. #2 | Critical Path: CP - 0.5∆MUX

## Slide 24
Impact on Timing
s6
s7
s4
s8
s12
s13
CP – 1.0∆MUX
CP – 0.8∆MUX
All paths within 2∆MUX delays from critical path shown above
CP – 1.0∆MUX
CP – 1.7∆MUX
CP – 0.5∆MUX
s9
CP – 1.3∆MUX
s10
CP – 1.5∆MUX
CP – 0.7∆MUX
Originally | Critical Path: CP
Trans. #1 | Critical Path: CP - 0.3∆MUX
Trans. #2 | Critical Path: CP - 0.5∆MUX

## Slide 25
Impact on Timing
s6
s7
s4
s8
s12
s13
CP – 1.0∆MUX
CP – 0.8∆MUX
All paths within 2∆MUX delays from critical path shown above
CP – 1.0∆MUX
s9
CP – 1.3∆MUX
s10
CP – 1.5∆MUX
CP – 0.7∆MUX
Already
transformed
Originally | Critical Path: CP
Trans. #1 | Critical Path: CP - 0.3∆MUX
Trans. #2 | Critical Path: CP - 0.5∆MUX
Trans. #3 | Critical Path: CP - 0.7∆MUX
Shortened critical path by 0.7 ∆MUX via 3 transformations

## Slide 26
Impact on Timing
s6
s7
s4
s8
s12
s13
CP – 1.0∆MUX
CP – 0.8∆MUX
All paths within 2∆MUX delays from critical path shown above
CP – 1.0∆MUX
s9
CP – 1.3∆MUX
s10
CP – 1.5∆MUX
CP – 0.7∆MUX
Already
transformed
Shortened critical path by 0.7 ∆MUX via 3 transformations
Limitation:
Critical path originating and terminating at the same FF

## Slide 27
Iterative Application of Transformations

## Slide 28
Scan Retiming Further
S_in
F_in
D
Q
Critical path
D
Q
D
Q
D
Q
Scan_en
Scan_en_del
shared
Scan_en_del
F_out
S_out
MUX delay transferred forward
Fanout delay transferred backwards
    Best case saving: Entire scan penalty
    (= MUX+fanout delay)
D
Q
D
Q
S_out
F_out
S_in
F_in
Critical path
D
Q
D
Q
Scan_en_del

## Slide 29
Experimental Results
High performance stream-cipher encryption circuits
 Higher reductions in critical path delay

## Slide 30
Conclusions
MUX and fanout delay transfer through proposed scan circuit retiming
  Can eliminate performance penalty of scan
  Clock paths untouched
Retains intact:
  Test development process (fault coverage, pattern count, etc)
  Test application process (test time, data volume, etc)
Few scan cells transformed  very small area cost