##### Compaction-Based Test Generation Using State and Fault Information

Ashish Giani *,  Shuo Sheng *,  Michael Hsiao *,  Vishwani D. Agrawal **

* Department of Electrical and Computer Engineering, Rutgers University, Piscataway, NJ 08854.

{ashishg, shuo, mhsiao} @ece.rutgers.edu

**  Bell Labs, Lucent Technologies, Murray Hill, NJ 07974

va@research.bell-labs.com

Abstract

We present a new test generation procedure for sequential circuits using newly traversed state and newly detected fault information obtained between successive iterations of vector compaction.  Two types of techniques are considered. One is based on which new states a sequential circuit is driven into, and the other is based on the new faults that are detected in the circuit between consecutive iterations of vector compaction. These data modify an otherwise random selection of vectors, to bias vector sequences that cause the circuit to reach new states, and cause previously undetected faults to be detected. The biased vectors, when used to extend the compacted test set, provide an intelligent  selection of vectors. The extended test set is then compacted.  Repeated applications of state and fault analysis, vector generation and compaction produce significantly high fault coverage using relatively small computing resources. We obtained improvements in terms of higher fault coverage, fewer vectors for the same coverage, or smaller number of iterations and time required, consistently for several benchmark circuits.

1. Introduction

Random test generation, proposed in [3], used a pseudo-random pattern generator to approximate the behavior of random patterns. As explained in [1], randomly generated patterns are useful for certain types of circuits, while they do not produce good fault coverage in other circuits. Further, they generally require a large test set size [2]. Certain lines in the circuit cannot be set to a specific logic value using purely random vectors, making faults on those lines hard to detect. These faults are called random pattern resistant faults. Weighted random patterns have been found to yield higher fault coverages in circuits that contain such types of hard to detect faults. Much work has been done on weighted random pattern generation [4,5]. In these approaches, the probability of getting a 0 or a 1 at a particular input is biased towards detecting random resistant faults. With weighted random patterns, the difficulty that arises is that no one set of weights may be suitable for all faults even in a combinational circuit. In the case of sequential circuits, the faults may need a biased internal state besides a biased input vector. So, it is more difficult to obtain a good set of weights at the primary inputs using only structural techniques. Static compaction procedures extract a set of "necessary" vectors from a given test set. Vector restoration techniques [6,7] aim to restore sufficient vectors necessary to detect all faults. Various methods to extend the compacted test set are given in [8,9], including randomly picking a vector from the compacted test set and holding it a given number of times, perturbing a few bits in a randomly chosen vector and holding it a given number of times, and copying over a sequence of vectors to generate new vectors. In these techniques, vectors are chosen randomly to extend the test set. In [10], the authors present a technique to generate tests for sequential circuits using weighted random vectors and a static compaction procedure while in [11], the correlation among test vectors was studied and this information was used to generate test vectors.

In our work, we would like to bias some "useful" vectors by making sure that they have a higher probability of being chosen. Thus, rather than having a purely uniform distribution of vectors, we introduce some non-uniformity into the process. Useful vectors are obtained using two broad categories. These are: New-State vectors that drive the sequential circuit into new states during successive iterations, and New-Fault vectors that obtain new faults during successive iterations. We show that with New State vectors, we are able to visit a greater number of useful (including previously unvisited) states in each iteration. This leads to the detection of more hard-to-detect faults in each iteration. So, we want to utilize and learn from the vectors that lead to the detection of these new states. We use this information obtained by analyzing the compacted set of vectors to intelligently choose useful vectors such that fewer vectors can achieve the same, or higher fault coverage in a smaller amount of time.

2. Overview of the Test Generation

Procedure

Figure 1 presents an overall picture of the Test Generation  Procedure using vector compaction. The algorithm is given below:

-Initialize iteration number i  to 0

-Generate L random vectors to form a random input

sequence S0

while (the terminating condition is not satisfied)

-Fault simulate Si on the circuit under test

-Apply static compaction on Si to obtain a

compacted test sequence Sic

-Extend the compacted sequence by generating

vectors to form a suffix Sisu

-Increment i for the next iteration

There can be three possible terminating conditions. These are: desired fault coverage is obtained, preset time for which the experiments were conducted is reached, and number of iterations of test set extension and compaction is reached. We chose the number of iterations as the terminating condition.

This paper focuses on methods of extending the compacted test set (i.e. obtaining suffix Sisu) by using New-State Prefix Vectors, New-State Postfix Vectors, New-Fault Vectors and Threshold-Fault Vectors.

3. Definitions

- New-State Prefix Vectors: A sequence of "m" vectors that lead to a newly visited state between consecutive iterations of compaction and fault simulation is called New-State Prefix (NSPR) Vectors. They are obtained as follows: Identify the different states that a circuit is driven into during two successive iterations. In iteration i, the states that were reached in iteration i-1 are compared with those that have been previously reached. NSPR vectors are the sequence of "m" vectors that lead to the new state. "m" is chosen to be the minimum circuit depth, which is the minimum number of Flip Flops on any path  from a primary input to a primary output. This information is recorded in the State Matrix.

- New-State Postfix Vectors: A sequence of "n" vectors that follow the vector that drives the circuit into a new state in consecutive iterations is called New-State Postfix (NSPO) Vectors.  "n" is chosen to be 5. This information is recorded in the State Matrix. Both NSPR and NSPO vectors are shown in Figure 2.

- New-Fault Vectors: A sequence of "m" vectors that lead to the detection of a new fault between consecutive iterations of compaction and fault simulation is called New-Fault (N-F) Vectors. They are obtained as follows: Identify the different faults that are detected during two successive iterations. In iteration i, the faults that were detected in iteration i-1 are compared with those that have been detected previously. N-F vectors are the sequence of "m" vectors that lead to the detection of the new fault. As before, "m" is chosen to be the minimum circuit depth.  This information is recorded in the Fault Matrix.

- Threshold-Fault Vectors: Vectors detecting faults equal to or greater than the threshold fault number are identified, and a sequence of "m" vectors prior to each of these vectors is called Threshold-Fault (T-F) Vectors. They are obtained as follows: Identify the number of faults detected by each vector. Set a threshold number of faults. The sequence of "m-1" vectors that occur prior to the vector that detects more faults than the threshold value, and the vector under consideration form the T-F vectors. As  before,  "m"  is  chosen  to  be  the  minimum sequential depth.  This information is recorded in the Fault Number Matrix. Both N-F and T-F vectors are shown in  Figure 3.

4. Test Generation Approach

Since the NSPR vectors lead to the detection of new states between consecutive iterations, they help span the state space of the circuit. Let us consider a circuit for which we have just visited a new state as depicted in Figure 4; exploring neighboring states of this newly visited state may help us in detecting faults that require one of these new states as an intermediate state to excite the fault, or propagate it to a primary output. As shown, there is a sequence of vectors (Vseq) that takes us from a relatively well explored state subspace, to a state that has not been previously visited. There may exist other sequences that take us back from this newly visited state to the previously explored subspace. Since the newly visited state detected a hard-to-detect fault, Vseq is a valuable sequence. We postulate that the state subspace around this state might be useful in detecting other previously undetected hard-to-detect faults. To do so, whenever some sequence takes us back to the previously explored state space, we would need to get back to the new unexplored subspace. However, it is not easy to do so, otherwise this region would have already been explored earlier. We know that the vector sequence Vseq had led us to the previously unvisited state earlier and can do so again. So, we bias it with a higher priority by choosing to bias the NSPR and NSPO as important vectors.

Similarly, the N-F vectors lead to the detection of new faults in consecutive iterations. This proves that they are useful in detecting hard-to-detect faults, because they are vectors that detect faults that could not be detected in earlier iterations. The T-F vectors that detect a large number of faults have already demonstrated their usefulness, so we use them to extend the compacted test set. We believe that these vectors, when compacted, might lead to the detection of more faults in subsequent iterations.

Algorithms for our two techniques are described below:

Technique 1: Using NSPR and NSPO Vectors.

While (number of vectors less than cut-off)

-Randomly pick a vector from the compacted

test set, perturb a few bits in it and hold it a

random number of times.

-Copy over a sequence of five vectors from

the compacted test set to generate new vectors.

-Randomly pick an NSPR/NSPO vector

from the State Matrix and copy over a

sequence of "m" vectors prior to this vector

and "n" vectors after this vector.

-From the State Matrix information

generated above, randomly pick an

### NSPR/NSPO vector, perturb a few bits in it

and hold it a random number of times.

Technique 2: Using N-F and T-F Vectors.

While (number of vectors less than cut-off)

-Randomly pick a vector from the compacted

test set, perturb a few bits in it and hold it a

random number of times.

-Copy over a sequence of five vectors from

the compacted test set to generate new vectors.

-From the Fault Matrix, randomly pick an

N-F vector, perturb a few bits in it and hold

it a random number of times.

-Randomly pick an N-F vector from the

### Fault Matrix, and copy over a sequence of

"m" vectors prior to this vector.

-Randomly pick a T-F vector from the Fault

Number Matrix, perturb a few bits in it and

hold it a random number of times.

-Randomly pick a T-F vector from the Fault

Number Matrix, and copy over a sequence

of "m" vectors prior to this vector.

We choose the cut-off value, the number of bits perturbed in a vector, and the number of times a vector is held in a similar manner as [8]. The cut-off value is initially set to 2,000 vectors. If two consecutive sequences do not detect any new faults, the cut-off is increased to the next higher value. Possible values that can be assigned to cut-off are 5,000, 10,000, 20,000 and 40,000. The cut-off is never increased beyond 40,000 because this would result in an excessive time for fault simulation while the compaction process occurs. Zero, one, two or three bits can be perturbed with equal probability in a vector. A vector can be held for 2i time units, with a probability of 2-(i+1) for 0 ( i (7, and 2-8 for i = 8.

5. Results

All experiments were conducted on an Ultra SPARC 10 with 256 MB of RAM for some ISCAS 89 and ITC 99 benchmark circuits.

The fault simulator used in our experiments targets all the faults in the circuit in each iteration. Other previously reported techniques target 128 [8] and 256 [9] randomly selected faults in the initial iterations, and gradually increase the sample size until all the undetected faults are targeted in later iterations. This leads to a disparity in the execution time taken for fault simulation during compaction. To remove this disparity and obtain a suitable platform for comparison, we implemented the algorithm suggested by [8] and used our fault simulator and compactor. As mentioned earlier, we fixed an upper bound of 125 iterations as the terminating condition.

Before going into the detailed results of our experiments, Figures 5, 6, 7 and 8 show the key idea of how the useful new states obtained from biasing NSPR and NSPO vectors can help in test generation. Figure 5 gives the total number of states visited in s382 during the first ten  iterations for our

technique   using   NSPR   and   NSPO   vectors,   versus  the

number of states reached for our implementation of the technique in [8]. Figure 6 shows the total number of faults detected in the s382 in the corresponding iterations for both techniques. For example, by iteration 2, our NSPR/NSPO technique has visited 1147 states, while the original implementation [8] visited 926 states. These 221 additional states helped to detect 9 additional hard faults in that iteration, as indicated in Figure 6. Consistently, our technique visits a greater number of new states and detects 363 faults by the sixth iteration, while our implementation of the technique in [8] required 10 iterations to reach the same number of faults. Thus, we are able to detect faults faster.

Likewise, Figure 7 gives the total number of states visited in the b11 during the first ten iterations for our technique using NSPR and NSPO vectors, versus the number of states reached for our implementation of the technique in [8]. Figure 8 shows the total number of faults detected in the b11 in the corresponding iterations for both techniques. As seen in these two figures, our technique visits a greater number of new states and detects more faults in a lower number of iterations when compared to our implementation of the technique in [8].

Going into detailed results, the results for the technique in [9] are shown in Table 1, while the results for our implementation of the technique in [8] are shown in Table 2. In Table 1, column 1 gives the circuit name, while columns 2, 3 and 4 give the number of faults detected, test set size, and the time taken to detect the indicated number of faults respectively. For example, for s382, 364 faults were detected with a test set size of 572. The time required was 0.46 minutes. In Table 2, columns 1 to 4 represent the same parameters as Table 1. Column 5 gives the number of iterations required to achieve the fault coverage.  For example, for s400, 382 faults were detected with a test set size of 617 vectors. 6 minutes and 9 iterations were required.

The results for our techniques are shown in Table 3. Column 1 gives the circuit name, while columns 2, 3, 4 and 5 give the number of faults detected, test set size, the time taken and number of iterations required to detect the indicated number of faults respectively for the technique in [8], columns 6, 7, 8 and 9 give these parameters for the technique using NSPR and NSPO vectors to extend the compacted test set, while columns 10, 11, 12 and 13 give these parameters for the technique using N-F and T-F vectors to extend the compacted test set.

Comparing the results obtained in Tables 1 and 3, we can see that for most circuits, our techniques require a smaller test set size to achieve the same high fault coverage. For example, in the technique using NSPR and NSPO vectors, the number of vectors required is about 13% less for the s526, about 16% less for the s1488, about 9% less for the s1494, and about 5% less for the b11 when compared to the method used in [9]. Comparing columns 3 and 7 of Table 3, the number of vectors required by this technique is about 34% less for  the  b01and about 57% less for the b04. We are also able to detect two more faults in the s400 and 393 more faults in the b21, and obtain 51 more faults and use about 35% less vectors for the b12 in comparison with the method used in [9].

In the technique using N-F and T-F vectors to extend the compacted test set, the number of vectors required is about 13% less for the s1494 when compared to the method used in [9]. Comparing columns 3 and 11 of Table 3, the number of vectors required by this technique is about 31% less for the b04, and about 25% less for the b08. We are also able to detect one more fault in the s400 and 180 additional faults using 751 less vectors for b21 in comparison with the method used in [9].

A possible explanation of why the technique in [9] requires fewer vectors than our techniques for certain circuits is that we used a Linear Reverse Order Restoration Algorithm mentioned in [8], but restored two vectors at a time, while the technique in [9] uses a Radix Reverse Order Restoration Algorithm.

Comparing the iterations taken for our implementation of the technique in [8] (Table 3, column 5), with the iterations required for our NSPR and NSPO technique (Table 3, column 9), we observe that the number of iterations required to achieve the fault coverage is about 38% less for the s382, about 68% less for the s526, about 59% less for the s1423 and about 80% less for the s1488 and s1494. Similarly, we obtain major improvements in the number of iterations required using N-F and T-F vectors (Table 3, column 13). Thus, we not only obtain savings in the test set size, but also need fewer iterations and less time to obtain the same high fault coverage.

| PREVIOUS METHOD [9] |
| --- |
| Circuit | Det. | Vec. | Time (min.) |
| s382 s400 s526 s713 s1196 s1238 s1423 s1488 s1494 s5378 b11 b12 b21 | 364 382 454 476 1239 1283 1416 1444 1453 3643 1004 1470 18023 | 572 677 1557 104 224 235 1049 426 454 672 419 3697 12651 | 0.46 0.65 2.64 0.13 0.4 0.44 8.84 1.93 2.2 35.55 1.59 27.49 135.72 |
|  | PREVIOUS METHOD [8] |
| Circuit | Det. | Vec. | Time (min.) | Iter. |
| s382 s400 s526 s713 s1196 s1238 s1423 s1488 s1494 s5378 b01 b04 b08 b11 b12 b21 | 364 382 454 476 1239 1283 1416 1444 1453 3643 133 1168 463 1004 1470 18023 | 641 617 1854 205 241 334 1387 549 508 672 91 416 422 496 3697 14946 | 26 6 51 4 13 18 171 59 89 840 0.5 14 9 22 292 6910 | 21 9 47 10 47 46 87 79 73 117 5 18 19 33 66 51 |

|  | A) [8] without fault samples | B) Using NSPR and NSPO vectors | C) Using N-F and T-F Vectors |
| --- | --- | --- | --- |
| Circuit | Det. | Vec. | Time (min.) | Iter. | Det. | Vec. | Time (min.) | Iter. | Det. | Vec. | Time (min.) | Iter. |
| s382 s400 s526 s713 s1196 s1238 s1423 s1488 s1494 s5378 b01 b04 b08 b11 b12 b21 | 364 382 454 476 1239 1283 1416 1444 1453 3643 133 1168 463 1004 1470 18023 | 641 617 1854 205 241 334 1387 549 508 672 91 416 422 496 3697 14946 | 26 6 51 4 13 18 171 59 89 840 0.5 14 9 22 292 6910 | 21 9 47 10 47 46 87 79 73 117 5 18 19 33 66 51 | 364 384 454 476 1239 1283 1416 1444 1453 3643 133 1168 463 1004 1521 18416 | 897 807 1349 85 229 245 1209 360 417 1412 60 180 390 399 2418 16139 | 12 7 21 0.5 15 13 60 15 6 155 0.1 3 2 20 93 3662 | 13 7 15 4 48 43 36 16 15 28 5 10 11 28 31 22 | 364 383 454 476 1239 1283 1416 1444 1453 3643 133 1168 463 1004 1516 18203 | 764 766 1548 79 245 290 1249 430 393 889 82 289 316 461 2400 11900 | 4 3 18 1 7 6 47 9 8 148 0.2 5 3 10 55 3651 | 7 9 14 4 28 25 31 16 16 32 3 15 14 18 25 35 |

6. Conclusions

We have proposed a new and efficient technique for extending the compacted test set, using information based on new states reached during successive iterations, and new faults detected between consecutive iterations. Our results show that, as in previous methods, high fault coverage was achieved.  In  some  cases, we detected more faults than have been previously reported. A significant improvement in fault coverage for the b12 and b21 was observed using both the NSPR/NSPO technique and the  N-F/T-F technique. At the same time, the number of vectors required to achieve the high level of fault coverage was fewer than other techniques required, while the number of iterations needed, and the time taken was also lower.

7.  References

[1] V. D. Agrawal, “When to Use Random Testing”, IEEE Trans. On Computers, vol C-27, No. 11, pp. 1054-1055, November 1978.

[2] M. Abramovici, M. A. Breuer and A. D. Friedman, "Digital System Testing and Testable Design", New York, NY: Computer Science Press, 1990.

[3] M. A. Breuer, "A Random and an Algorithmic Technique for Fault Detection Test Generation for Sequential Circuits", IEEE Trans. On Computers, vol C-20, No. 11, pp. 1364-1370, November 1971.

[4] M. F. Alshaibi and C. R. Kime, "Fixed-biased pseudo-random built in self test for random pattern resistant circuits", in Proc. Intl. Test Conf., Oct. 1994, pp. 929-938.

[5] F. Muradali, T. Nishada, and T. Shimizu, "Structure and technique for pseudo random-based testing of sequential circuits", in Journal of Electronic Testing: Theory and Applications (JETTA), Feb. 1995, pp. 6:107-115.

[6] I. Pomeranz and S. M. Reddy, "Vector restoration based static compaction of test sequences for synchronous sequential circuits", Proc. International Conference on Computer Design, pp. 360-365, Oct. 1997.

[7] R. Guo, I. Pomeranz, and S. M. Reddy, "Procedures for static compaction of test sequences for synchronous sequential circuits based on vector restoration", Proc. Design, Automation, and Test in Europe (DATE) Conf., pp. 583-587, Feb. 1998.

[8] R. Guo, I. Pomeranz, and S. M. Reddy, “A fault simulation based test pattern generator for synchronous sequential circuits”, 17th IEEE VLSI Test Symposium (VTS), pp. 260-267, April 1999.

[9] R. Guo, S. M. Reddy and I. Pomeranz, “PROPTEST: A Property Based Test Pattern Generator for Sequential Circuits Using Test Compaction”, Proc. Design Automation Conference (DAC), pp. 653-659, June 1999.

[10] A. Jain, V.D. Agrawal, M. S. Hsiao, "On generating tests for

sequential  circuits  using  static  compaction",  ITSW  1999,

March 1999.

[11] A. Giani,  S.  Sheng,    M.  S.  Hsiao,   and   V.  D.  Agrawal,

"Correlation-Based Test Generation for Sequential Circuits",

Proc.   9th  IEEE  North  Atlantic  Test  Workshop (NATW),

pp. 76-83, May 2000.

# Text boxes

Input Sequence

Si

Compacted Test

Sequence Sic

Fault simulation  based

compaction

Vector Sequences

Termination

Condition

Satisfied ?

Condition

satisfied?

No

Sic  +

suffix Sisu

Yes

Stop

Figure 1: Overview of Test Generation

Vector at which the circuit was driven into a new state

Compacted test set

# Figure 2: New-State Prefix and New-State

Postfix Vectors

“n” New-State Postfix (NSPO) Vectors

“m” New-State Prefix  (NSPR) Vectors

:

:

:

:

:

:

:

:

“m” New-Fault  (N-F) Vectors

“m” Threshold-Fault

(T-F) Vectors

Compacted test set

Vector at which a new fault was detected

Vector which detected > threshold number of faults

:

:

# Figure 3: New-Fault and Threshold-Fault Vectors

# Table 1: Results reported in [9]

Table 2: Implementation of the original algorithm

in [8] without fault samples

# Figure 8: Total Faults detected for b11

Figure 7: Total States visited for b11

Figure 6: Total Faults detected for s382

# Figure 5: Total States visited for s382

Table 3: Results for: A) Algorithm in [8] without fault samples, B) NSPR and NSPO

Vectors and C) N-F and T-F Vectors

Det. = Faults Detected

Vec. = # Vectors in Test Set.

Det. = Faults Detected    Vec. = # Vectors in Test Set.

Iter. = # Iterations required

Det. = Faults Detected     Vec. = # Vectors in Test Set.    Iter. = # Iterations required

Previously visited state sub-space

Newly reached state

Unexplored subspace around newly reached state

#### Total State Space

Newly visited state

Vseq

Figure 4: Reasons for biasing NSPR and NSPO

vectors