# Minimum Dynamic Power Design Using Variable Input Delay CMOS Logic

Vishwani D. Agrawal

Auburn University

Department of Electrical and Computer Engineering

Auburn, AL 36849, USA

Complete elimination of all unnecessary power-consuming glitches in a digital circuit requires a careful adjustment of gate delays as well as insertion of delay buffers. Although the power dissipation is significantly reduced, the buffers consume some power. A new variable input-delay CMOS technology allows glitch removal without buffers and hence leads to the minimum dynamic power design at the highest clock frequency possible for the technology used. Variable input-delays are obtained by inserting suitably sized series transistors at the logic gate inputs. Complete design, layout and spice simulation (see figure) of the benchmark circuit c7552 shows a dynamic power saving of 68% peak or 58% average over an unoptimized circuit. The talk ends with a preview of the ongoing research on leakage power reduction in submicron technologies.

This research was conducted at Rutgers University with support under an NSF grant.

Vishwani D. Agrawal is the James J. Danaher Professor of Electrical and Computer Engineering at Auburn University, Alabama, USA. For his details see website http://www.eng.auburn.edu/~vagrawal.